## Slide 1: Energy Reserve Budgeting for CubeSat’s with Integrated FPGA
Scott Sterling Arnold, Ryan Nuzzaci, and Ann Gordon-Ross
University of Florida
Department of Electrical and Computer Engineering

## Slide 2: CubeSats
CubeSats are nano-satellites categorized by size and weight
  1U: 10cm x 10cm x 10cm and less than 1Kg
  2U: 10cm x 10cm x 20cm and less than 2Kg
  3U: 10cm x 10cm x 30cm and less than 3Kg
Limited surface area restricts area for solar panels and power production capabilities
  1U: 1-2.5 Watts; 2U: 2-5 Watts; 3U: 7-20 Watts
Power budgets
  Ensure CubeSat’s subsystems’ power usage does not exceed power production
  Primary CubeSat subsystems:
    Attitude determination and control (ADCS)
    Command and data handling (C&DH)
    Communications
    Electrical power supply (EPS)
    Technical payload
Sample 1U power budget

## Slide 3: Shifting Trends in CubeSat Usage
Typical, past CubeSat mission scopes
  Commercial-off-the-shelf (COTS) component testing in space environment
  Novel technology testing (e.g., ion thrusters, radiation detectors)
  Telemetric sensor data acquisition (e.g., atmospheric data, GPS locating)
Increasing interest in CubeSats due to proven mission successes and low-cost imposed by strict design standards
  Academic
    CP1 (2001) – COTS technology in space verification
    Quakesat (2003) – Early earthquake detection
    M-Cubed (2012) – Rad-hard FPGA evaluation in space
  Small countries and companies
    INTA and EU
    Boeing and The Aerospace Corporation
New, emerging CubeSat mission scopes
  Trending towards useful scientific data acquisition (i.e., increased high-performance requirements for on-board data processing)
  Trending away from simple verification and usage experiments

## Slide 4: FPGAs for High-Performance Data Processing
Field-programmable gate arrays (FPGAs)
  FPGAs exploit algorithm parallelism (e.g., matrix multiplication, sorting, image processing)
  Highly parallelizable applications show significant speed-up with respect to microprocessors
FPGAs for space-oriented applications
  Hyperspectral Imaging: 15x speed-up for FPGA vs. microprocessor
  Synthetic Aperture Radar: 6x speed-up and 1/3 of the power for FPGA vs. microprocessor
Challenges with leveraging FPGAs in CubeSats
  FPGA’s high power usage relative to other lower power processing elements
  FPGA’s static power usage causes continual strain on system power budget
Notes: OKAY

## Slide 5: Integrating FPGAs into CubeSats
Challenge: Traditional FPGAs are too high power for CubeSats
Solution: Increasing design focus on lower power FPGAs
  However, low-power FPGAs still typically have greater power usage than microprocessors
Even with low-power FPGAs, subsystem power usage must be carefully budgeted
  Can reduce subsystems’ power consumption and/or operational time to accommodate FPGAs
Power budgeting
  Over-simplifies power usage requirements
  Does not account for subsystem usage over time
We present a method that aids in FPGA integration for subsystem management, which also provides:
  Quantitative methods for determining time payload is usable
  An early-stage design aid to optimize power usage and reduce the risk of late system redesign
  Enhanced design stage view of CubeSat performance

## Slide 6: Energy Reserve Budgeting
We propose a method called energy reserve budgeting
  Leverage CubeSat subsystem usage with the data handling power of FPGAs
  Mathematically predict operational time of FPGA payloads early in CubeSat developmental process
  Evaluate appropriate CubeSat subsystems for use with FPGA payloads
  Identify orbits that allow for payload to be effective based on mission requirements
Energy reserve budget leverages multiple power budgets, called power modes, to evaluate the payload operational time given a particular orbit
Example power modes
  Power-Storing mode
    Minimal communications active
    No payloads active
    Single storing mode per energy reserve budget
  Overpower mode(s) (one or more)
    Payloads active and performing mission tasks
    Communications uplink and downlink to communicate with ground station
    Multiple overpower modes require operational time management to evaluate payload usage

## Slide 7: Analysis and Orbital Mechanics
Orbital mechanics used to determine eclipse time and total energy per orbit
  CubeSat eclipse time limits the amount of energy stored
  Determining energy per orbit allows for evaluation of power modes
Circular orbit’s eclipse time is dependent on:
  Altitude – Satellite height above sea-level
  Inclination – Satellite angle with respect to equator in eastward direction
  Right ascension of the ascending node – Satellite angle when crossing the equator in the direction of ascent with respect to the vernal equinox
  Right ascension and declination of the Sun – Time-of-year dependent

## Slide 8: Orbital Patterns for Testing
Orbital evaluation determines CubeSat suitability to a particular orbit
Sample orbits for analysis
  Two best-case Sun-synchronous orbits: no eclipse time, optimal energy storage
  One worst-case orbit at low altitude
  Other orbits chosen randomly for comparison purposes
From altitude and inclination, we evaluate orbits for eclipse time (ts)
  Right ascension of the ascending node/satellite (RAAN) - determined at time of Epoch
  Beta-range - Angle of the orbital plane of the satellite to the Sun’s orbital plane
  ts – CubeSat’s eclipse time in minutes during a single orbit

## Slide 9: Contributions
We provide a simple system design evaluation method, using energy reserve budgeting, to better integrate high-power consumption components into CubeSats
  Evaluate our method using two case studies: 1U case study presented here; 3U case study detailed in the paper
Demonstrate that low-power COTS FPGAs can be integrated into CubeSats for increased data processing performance
  Leverage power results from our experiments
  Balances FPGA power with subsystems to attain optimal CubeSat performance
  Assists in subsystem redesign if power budget is not met
Experimental results using realistic FPGA power usage for Canny-edge detection image processing
  Reveals what a CubeSat designer can expect from leveraging FPGAs
  Numerically demonstrates the integration of low-power FPGAs in CubeSats

## Slide 10: Experimental Setup
Determine FPGA power usage
  Simulate realistic usage of FPGA for space systems
  Create image filter application to run on FPGA
FPGA power assessment tools
  Application built using Xilinx ISE-Webpack
  Power consumption obtained with Xpower analyzer
Energy reserve budget exemplified
  Evaluate usefulness with respect to CubeSat subsystem design
  Shows potential for leveraging FPGAs in CubeSats
1U case study
  Evaluate subsystem utilization, performance, and operational time
  Subsystem power usage and mission’s required operational time from literature
Energy reserve budgeting:
  Determine payload operational time
  Decide on system redesign
  Reevaluate energy reserve budget

## Slide 11: Data Processing Power Consumption
Canny filter used to assess FPGA power during data processing
  Xpower analysis using vcd file, which records hardware bit flips
  Vcd files provide a more accurate power consumption for FPGAs
Systems with on-board camera use filtering and pre-processing
  Satisfy memory constraints
  Reduce image size for downlink
  FPGAs well suited for parallelizable image processing
Case study application - Canny-edge detector
  Multiple filtering stages for edge detection

## Slide 12: Canny Edge Detection Results
Canny filter application shows power and FPGA computational resource usage
  Spartan-3 FPGA devices evaluated for low-power and high-performance
  Virtex-4 FPGA devices evaluated for non low-power comparison to the Spartans
Lowest power FPGA usage = 137.63 mW
Computational resource usage assists in quickly evaluating alternate/more devices
  Allows for inclusion of more FPGAs using the same filter and power estimation software
  System designer can see additional room for increasing application size if desired
Power consumption by device
Computational resource usage by device family

## Slide 13: 1U Case Study Setup
1U case study based on the M-Cubed project [1]
  Secondary payload: Virtex-5QV Single event Immune Reconfigurable (SIRF) FPGA
  CubeSat On-board Validation Experiment (COVE) mission used the Virtex-5QV
  Passive Magnetic Attitude adjustment, which required no power
M-Cubed designers recognized high power as a concern
  COVE payload study shows power usage between 4-6 Watts on average [2]
COTS FPGA usage in 1U case study
  We replace COVE payload with a low-power Spartan XC3S400A FPGA
[1]D. Bekker, T. Werner, T. Wilson, P. Pingree, K. Dontchev, M. Heywood, et al,”A CubeSat design to evaluate the Virtex-5 FPGA for Spaceborne Image Processing,” Aerospace Conference, 2010 IEEE, Big Sky, MT, 6-13 March 2010
[2]P. Pingree, T. Werne, D. Bekker, T. Wilson, J. Cutler, M. Heywood, ”The Prototype Development Phase of the CubeSat On-board processing Validation Experiment” in IEEE Proc. 2011 Aerospace Conference, Big Sky, MT, 2011
M-Cubed 1U power budget [1]
Notes: TODO: add full refs

## Slide 14: 1U Energy Reserve Budget
Energy generated
  2,010 mW generated power in sunlight
Mission’s communication time requirements
  5 minutes downlink, 10 minutes uplink
  Translates to 5 minutes per orbit in communication-overpower and uplink-overpower modes
Evaluate processing-overpower mode’s operational time
1U Case study energy reserve budget
Power-storing mode
  Active C&DH for power mode changes
Communication-overpower mode
  Fully active uplink and downlink
Uplink-overpower mode
  Active uplink only
Processing-overpower mode
  FPGA and camera active
  C&DH assisting in data storage

## Slide 15: Energy Reserve budget analysis
Using Eqn1. and Eqn2.
  Total energy generated by solar panels
  Determine payload operational time in orbit
Energy reserve budget analysis
  Only Sun-synchronous orbits show positive payload operational time
  All other orbits show negative time
If power budget remains unchanged
  Severely limits orbit options and launch opportunities
  Designers continue with next stage of CubeSat development (construction)
Options to expand orbit options:
  Reduce subsystem power usage
  Reduce time spent in other overpower modes (use Eqn3.)
  Redesign/replace entire subsystems
Processing-overpower operational time in minutes during a single orbit
Eqn1. Energy produced during a single orbit
Eqn2. Payload-overpower mode operational time per orbit
Eqn3. Generalized formula for overpower mode operational time per orbit

## Slide 16: Conclusions and Future Work
Energy reserve budgeting for CubeSats optimizes power usage and performance
  Addition power optimization case study in paper using a 3U CubeSat based on the QuakeSat mission
Presented a simple system design evaluation method that assists designers in integrating high-power consumption components (i.e., FPGAs) into CubeSats for high-performance on-board data processing
  Presented examples of realistic FPGA power usage for Canny-edge detection
  Experiments show successful integration of low-power COTS FPGAs
  Quick calculation of payload operational time with respect to orbit
  Assists designers in maximally leveraging FPGAs (i.e., maximizing payload operational time) in CubeSats
Future work
  FPGAs trending towards lower power, thus better suited for future CubeSats
    Early evaluation of 7-Series Xilinx components indicate an even heavier focus on low power than the previous low-power components
  Expand energy reserve budget analysis to include additional high-performance processing components