## Slide 1: A Framework to Analyze, Compare, and Optimize High-Performance, On-Board Processing Systems
Nicholas Wulf
Alan D. George
Ann Gordon-Ross
3/5/2012

## Slide 2: On-Board Proc. Framework
Goal: Provide theory for determining Pareto-optimal device & fault-tolerant (FT) strategy for on-board processing systems
  Focus on small satellites, UAVs, smart munitions, AUVs
  Generalized comparison framework deters ad hoc design methodology, leading to Pareto-optimal designs
Approach: Divide exploration space into its key components for study
  Device Set – Includes CPUs, DSPs, FPGAs, GPUs, & any Rad-Hard versions
  FT Strategies – Sacrifice resources for fault tolerance (may be app-specific)
  Mission Characteristics – Defines system’s environmental conditions
  Application Set – Includes most common kernels (e.g., space apps.)
  Analysis – Design evaluation metrics calculated from other components
    Is selected design acceptable?
    How does it compare to others?
Device Set
FT Strategy Set
Mission Characteristics
Application
Kernel Set
Analysis

## Slide 3: Calculating Computational Density
Computational Density (CD) used to analyze device performance
  Developed within CHREC at the University of Florida
  Applicable to wide range of architectures (e.g., CPU, DSP, GPU, FPGA, etc.)
  Produces results in terms of operations per second
    Different CD result for each type of precision (e.g., bit, 8-bit int., 64-bit double)
    CD also depends on type of operation (e.g., add, multiply, divide)
Standard objective methodology for calculating CD on FPGAs
  Generate and analyze compute core on FPGA
    Perform twice for each core; one with and one without DSP resources
    Core must match desired precision & operation
  Collect data on resources used and max freq.
  Use optimal packing algorithm to determine maximum number of cores on device
  CD equals number of cores times worst clock rate from the list of cores used

## Slide 4: Framework Methodology
0.10
0.14
13.89
Designs evaluated according to two metrics
Power – power consumed by device
  Sensor data rate & application determine amount and type of required processing
  Device utilization is ratio of corresponding device CD to required processing
  FT strategy overhead increases utilization
  Linear interpolation between power range to find power consumption
Dependability – time between failures
  Device radiation characteristics and environment determine device upset rate
  Low utilization causes lower vulnerability
  FT strategies help to mitigate upsets
Dependability
72%
Consumed
Device
Power
Sensor
Utilization: 24%
Utilization: 72%
Device
TMR
100%
0%
50%
Static
Max
Utilization
Device Cross-Section (SEE / Particle·m2)
Environmental Radiation (Particles / m2·ster·s)
Power
LET
100
50
0
Device Upset Rate:
10 upsets/day
Only 72% of device is vulnerable
TMR protects against 99% of upsets
MTBF:
days
Sensor
Dependability
MTBF = Mean Time Between Failures
TMR = Triple-Modular Redundancy
CD = Computational Density

## Slide 5: HSI Case Studies
Hyperspectral Imaging (HSI) enables detection of key materials within a scene
  Detects intensities of hundreds of wavelengths for each pixel forming an image cube
  Compares characteristic spectrum of pixels to spectral signatures of desired materials
  Marks location of identified materials within the scene
Image cube too large for transfer to processing station due to limited bandwidth
Solution: perform computation in-situ and only transfer final results
Two HSI missions chosen as case studies for on-board processing
  Hyperion on EO-1 satellite requiring 2.2×109 32-bit integer MAC/s
  AVIRIS on ER-2 aircraft requiring 348×106 32-bit integer MAC/s
Detect
Compare
Identify
MAC = Multiply Accumulate

## Slide 6: Raw Results
Studied design combinations of 6 FPGAs and 3 fault-tolerant strategies
  Devices: 3 standard Virtexes, 2 low power Spartans, and 1 Rad-Hard SIRF
  Fault-tolerant strategies:
    No fault tolerance (NFT): 0% overhead and no added reliability
    Algorithm-based FT (ABFT): 10% overhead and significant added reliability
    Triple-modular redundancy (TMR): 200% overhead and strongest reliability
Power consumption and dependability metrics calculated for each design
FPGA = Field-Programmable Gate Array
Values predicted with linear regression on feature size in underlined italics

## Slide 7: Optimal Design Selection
Framework determines Pareto-optimal designs based on metrics
  Non-Pareto-optimal designs can be completely ignored
Constraints on metrics enforced to remove invalid designs
  Removes unreliable and/or power-hungry designs based on mission
Out of 18 designs, only 5 designs selected as optimal for each mission
  Designers decide which design is best based on desired tradeoffs
EO-1 Hyperion Satellite
ER-2 AVIRIS Aircraft

## Slide 8: Conclusions and Future Research
Conclusions
  The design of on-board processing systems can be complicated
    Many constraints due to sparse and hostile environments
    Many combinations of devices and FT-strategies to consider
  Our framework simplifies exploration space and highlights most promising designs, allowing designers to choose best design for their needs
Future Research
  Add CPUs to list of studied devices (from high performance to low power)
  Consider memory devices in addition to processors
    Integral to on-board processing systems
    Affects performance, power, and dependability
  Expand framework to include metrics such as lifetime (TID), cost, size/weight, maximum dose rate