## Slide 1: Bitstream Relocation with Local Clock Domains for Partially Reconfigurable FPGAs
Adam Flynn, Ann Gordon-Ross, Alan D. George
NSF Center for High-Performance Reconfigurable Computing (CHREC)
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: Partial Reconfiguration
Full Reconfiguration
  Bitstream for entire FPGA is loaded onto FPGA
Partial Reconfiguration (PR)
  Only certain portion(s) of FPGA are reprogrammed with smaller application modules
  Advantages
    Shorter reconfiguration time
    Less power
    Smaller bitstreams
    Rest of FPGA remains operational
FPGA
Peripheral links can be maintained during reconfiguration
Design A
Reconfigurable Region
Design B
Module A
Reconfigurable Region
Module B
Module C
Module D
Radio Link
Video Link

## Slide 3: PR Terminology
Partial Reconfiguration Region (PRR)
  FPGA fabric is partitioned into multiple reconfigurable regions.
Partial Reconfiguration Module (PRM)
  Application modules
  Loaded into PRRs on-the-fly
  Multiple PRMs can map to each PRR
Static Region
  Fixed, base design logic
  Remains operational during reconfiguration
Bus Macro
  Pre-placed, pre-routed macro to route signals between PRMs and the static region
PRR
PRR
Static
PRM A
PRM C
PRM B
PRM D
PRM B
PRM D

## Slide 4: Basic Problem with PR
Each PRM to PRR mapping requires unique partial bitstream
  Multiple bitstreams must be stored for each module
  Unnecessary overhead
Bitstream Storage
Static
PRR 2
PRR 1
PRMA_PRR1
PRMB_PRR1
PRMA_PRR2
PRMB_PRR2
FPGA

## Slide 5: Solution - Bitstream Relocation
Partial bitstream is manipulated to change physical location on FPGA
[write] - Frame Address (FAR) register.
Top/Bottom: Top.
Resource type: CLB/IO/CLK.
Row number: 2.
Column number: 2.
Minor address 3.
Changing FAR address column from 2 to 3.
Changing FAR address row from 2 to 0.
Sample SW Terminal Output
PRR
PRR
PRR
PRR
FPGA
Module
Static
Module
Module
Module
Module

## Slide 6: Bitstream Relocation (BR)
Benefits
  Increased flexibility in time-multiplexing FPGA resources
  Reduced bitstream storage requirements
  Bitstream migration between devices
  Ability to move modules away from faults
Bitstream Storage
PRM A
PRM B
Static
FPGA
PRR 1
RRR 2
PRR 3
PRR 4
Bitstream
Relocator
Bitstream Storage
PRM B/PRR 4
PRM B/PRR 3
PRM B/PRR 2
PRM B/PRR 1
PRM A/PRR 4
PRM A/PRR 3
PRM A/PRR 2
PRM A/PRR 1
Eliminates need for multiple copies of same partial bitstream
No relocation
With relocation

## Slide 7: Motivating Application Domains
Module A
Decision Logic
Module A
Module A
Module B
Module B
Module B
2x Triple Modular Redundancy (TMR)
Module A
Decision Logic
Module A
Module B
Module B
Module C
Module C
3x Self Checking Pair (SCP)
Reconfigurable fault tolerance & adaptable component-level protection
Fault tolerance mode can adapt to current conditions
PRRs can be reconfigured to desired protection/performance level
Virtual Architecture for PR
Framework for online module placement and scheduling
Peripheral interface(s) and inter-module communication infrastructure statically defined
Multiple benefits of bitstream relocation:
Flexibility for on-the-fly placement and scheduling of modules
Reduced bitstream storage/communication requirements

## Slide 8: Clock Domains
Local Clock Domains (LCDs)
  One global clock signal
  Leverage regional clock resources in Virtex 4/5 FPGAs
  Upgrade to existing clock infrastructure techniques necessary for bitstream relocation
  Clock frequency specified at PRM level
  Provides a finer-grained control of multiple clock domains
Multiple global clock domains
Each unique PRR clock frequency requires a global clock signal
MUX in each PRR selects intended frequency
Imposes overheads such as increased power consumption
PRR
PRR
Multiple Clock Domains w/o LCDs
PRR
PRR
Static
MUX (CLBS)
PRR
PRR
Multiple Clock Domains w/ LCDs
PRR
PRR
Static
BUFR

## Slide 9: Power Consumption Improvement
Power consumption improvement scales at approximately 3-4 mW/domain
* Clock frequency was held constant across domains for comparison
Chart: Clock Power (mW)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0
w/ LCDs | 19.22 | 25.36 | 29.35 | 34.77 | 38.04 | 42.03 | 43.87 | 47.14 | 48.62 | 52.61 | 57.67 | 70.85
w/o LCDs | 19.22 | 28.88 | 36.38 | 45.31 | 52.1 | 59.61 | 64.96 | 71.75 | 76.75 | 84.25 | 92.83 | 109.53
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0
w/ LCDs | 28.84 | 38.04 | 44.02 | 52.15 | 57.06 | 63.04 | 65.8 | 70.71 | 72.93 | 78.92 | 86.51 | 106.28
w/o LCDs | 28.84 | 43.31 | 54.57 | 67.97 | 78.15 | 89.41 | 97.45 | 107.63 | 115.12 | 126.38 | 139.24 | 164.29
Number of Clock Domains

## Slide 10: Increased Max Clock Frequency
Chart: Frequency (MHz)
| avg | echo | flanger | passthru | pulsate | static
Global | 151.1487 | 122.6392 | 212.5399 | 306.6544 | 211.1932 | 104.1233
LCD | 144.6341 | 132.714 | 190.0418 | 182.8822 | 114.4034 | 104.3406
Bus Macro | 126.2786 | 115.8346 | 150.4664 | 168.4069 | 128.3368 | 97.2195
10-15% average increase for LCD vs. Bus Macro
Max Clock Frequency for PR Audio Filter Design Modules
Global: clock signals routed globally
  Not compatible with BR (no consistent clock signal interface across PRRs)
LCD: clock signals routed through regional clock resources
  Compatible with BR (regional clock resources provide consistent signal interface)
Bus Macro: clock signals routed through bus macros
  Compatible with BR (bus macros provide consistent signal interface)
  Introduces routing inefficiencies that degrade max frequency