## Slide 1: VAPRES A Virtual Architecture for Partially Reconfigurable Embedded Systems
Presented by Joseph Antoon
Abelardo Jara-Berrocal, Ann Gordon-Ross
NSF Center for High-Performance Reconfigurable Computing (CHREC)
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: Adaptive Hardware Applications
Kalman filter used for target tracking
  Finds likely location from noisy measurements
  Optimized filter depends on target type
Slow Target
Low Power | Constant gain
Low Bandwidth | Kalman Filter
Fast Target
High Power | Constant gain
High Bandwidth | Kalman Filter
Airborne Target
High Power | Variable Gain
Low Bandwidth | Multi-scale Smoother
Noisy Target
High Power | Variable Gain
Low Bandwidth | Kalman Filter

## Slide 3: Adaptive Hardware Applications
FPGAs often out-perform CPUs
  Parallel computing power
  Kalman filters scale well
Partial Reconfiguration (PR)
  Run-time HW adaptation
  Allows FPGA time-sharing
Communication Challenge
  Transfers between modules can lock up CPU
  Inter-module network alleviates resources
Processor
CPU
FPGAs
FPGA Device
CPU
Memory
Filter A
Filter B

## Slide 4: Using Partial Reconfiguration
2. Platform studio
3. Import into ISE
6. Code PR
region HDL
System Specifications
1. Define system
5. Set PRRs as black boxes
top
static
prr_a
prr_b
4. Divide project into mandated hierarchy
7. Synthesize!
9. Map on to PlanAhead
8. Guess Estimate
a good floorplan
12. Write software
11. Implement!
10. Create “configurations”
Could you make it just a bit different…

## Slide 5: Identifying Issues With PR
Support
  Only supported by Xilinx
  Altera support announced
Lack of abstraction
  Manual partitioning
  Manual floor-planning
App-specific architectures
  Increased time-to-market
  Reduced flexibility
Frustrating
Design Flow!
In this work, we propose VAPRES
  A Virtual Architecture for PR Embedded Systems
  Abstracts base system from application
  Automates design flow and floor-planning
  Scalable, flexible features

## Slide 6: VAPRES Architecture
MicroBlaze CPU
PR
Region 1
PR
Region 2
PLB Bus
DCR
Bridge
PR Socket
PR Socket
FSL
Fast
Simplex
Links
Switch 1
Switch 2
IF
IF
IF
IF
IO
Module
To IO
MicroBlaze CPU
PR
Region 1
PR
Region 2
PLB Bus
DCR
Bridge
PR Socket
PR Socket
FSL
Fast
Simplex
Links
Switch 1
Switch 2
IF
IF
IF
IF
IO
Module
To IO
  PR Regions (PRRs)
    Independent clocks
    FIFO-based I/O
    Online placement
    Created separately
  MACS
    Intermodule network
  Flexible, scalable
    PR Region Count
    PR Region Size
    MACS bandwidth
      Module channel width
      Left to right channel width
      Right to left channel width
    IO Module Count
MicroBlaze CPU
PR
Region 1
PR
Region 2
PLB Bus
DCR
Bridge
PR Socket
PR Socket
FSL
Fast
Simplex
Links
Switch 1
Switch 2
IF
IF
IF
IF
IO
Module
To IO

## Slide 7: PR Region Connectivity
PR
Region
MicroBlaze
MACS Switch
FSL
Fast Simplex
Links
Producer / Consumer Queues
Slice Macros
Slice Macros
PR Socket
Device Control Register (DCR)
Clock
Macro
PRR
FSL
Enable
Reset
Clock
Select
Regional Clock Buffer
(BUFR)
Fast Clock
Slow Clock
Clock Multiplexer
(BUFGMUX)

## Slide 8: MACS – Intermodule Network
Minimal Adaptive-Routing Circuit Switched Network
Circuit based
  Uses streaming channels
  Circuit set by first word in channel
  Fast setup (<10 cycles)
Switch 2
IF
IF
Module 2
Module 1
Switch 2
IF
IF
Module 3
dst
end

## Slide 9: Design Methodology
Two separate design flows
  Base System
  Application
Applications made independently
  Only base system specs needed
Base Flow
App Flow
App Flow
App Flow
Base system specifications

## Slide 10: Base System Design Flow
System
Specs
User feeds specs to VAPRES
Base design created from specs
  Parametric templates used
System files generated
  Floorplan and Constraints
  Embedded Dev. Kit (EDK) Files
  HDL
Synthesis
Implementation
Bitstream generated
System downloaded to the board
Base system flow
Generate Bitstream
Implementation
Synthesis
HDL
Floorplan
Base Design
Templates

## Slide 11: Application Design Flow
Application Flow
Executable
Link
Synthesis
Generate Bitstream
Implementation
System
Specs
Partition App
  Hardware
  Software
Software flow
  Compile
  Link
Hardware Flow
  Synthesize
  Implement
  Bitstream gen
Download App
API
Compile
Application Decomposition
HDL
Source Code

## Slide 12: Revisiting Target Tracking
MicroBlaze CPU
Blank
PR Region
PLB Bus
DCR
Bridge
PR Socket
Switch 2
IF
IF
IO
Module
Sensor
ICAP
Filter
Storage
Aerospace Kalman Filter
Looks like a
spaceship
Aerospace Kalman Filter

## Slide 13: Seamless Filter Swapping
MicroBlaze CPU
Blank
Module
SW2
IF
IF
IO
Module
SW2
IF
IF
Blank
Module
Filter tracks target
  Target slows down
  Filter swap needed
First load new filter
  Spare region used
  Old filter continues
Redirect traffic
  Downtime is now negligible
  Previously in seconds
High Power Kalman Filter
Low Power Kalman Filter
Low Power Kalman Filter
Low Power Kalman Filter
Low Power Kalman Filter
The target changed!

## Slide 14: Experimental Setup - Resources
Post Place and Route
Implemented on ML401 board
  Virtex-4 LX25 FPGA
VAPRES
  Two PR Regions
  16x11 CLB region size
  Two IOMs
MACS
  Four switches
  32-bit channels
  Two channels left to right
  Two channels right to left
Floor Plan
Base System View

## Slide 15: Results – Resource Usage
Chart: VAPRES Resource Usage
| MicroBlaze | MACS
Slices | 9721 | 1890
9721
1890
Chart: 
| MicroBlaze | MACS | Remaining
Resource Usage | 0.28 | 0.06 | 0.66
LX60
Chart: 
| MicroBlaze | MACS | Remaining
Resource Usage | 0.67 | 0.14 | 0.19
LX25
Chart: 
| MicroBlaze | MACS | Remaining
Resource Usage | 0.17 | 0.04 | 0.79
LX100

## Slide 16: Experimental Setup – Timing
Flash
BRAM
ICAP
Two methods to reconfigure
  Implemented in software
  1) Write bitfile in one stage
  2) Write bitfile in two stages
One-stage method
  Load Flash sector to BRAM
  Write to ICAP
  Repeat until bitfile is loaded
Two-stage method
  Load bitfile into BRAM
  Write bitfile to ICAP
Less RAM
required
Load once,
write often
ICAP
BRAM
Flash
Board peripheral
FPGA structure

## Slide 17: Results – Reconfiguration Time
Chart: 
| One-Stage | Two-Stage
Loading + Writing | 1.043 | 0
Loading | 0 | 0.99398
Writing | 0 | 0.07194
Chart: 
| Loading Flash | Writing ICAP
Resource Usage | 0.93251 | 0.067491
Two-Stage
Time Breakdown
Chart: 
| MicroBlaze | MACS
Resource Usage | 0.953 | 0.047
One-Stage
Time Breakdown
ICAP write reduced to 71.94 ms

## Slide 18: Experimental Setup - Scaling
Four VAPRES Systems Set Up
Small
PRRs: 1
Width: 10 CLB
Height: 1 row
MACS: No
Medium
PRRs: 1
Width: 10 CLB
Height: 2 rows
MACS: No
Large
PRRs: 2
Width: 16 CLB
Height: 2 rows
MACS: Yes
Populous
PRRs: 3
Width: 16 CLB
Height: 1 row
MACS: Yes

## Slide 19: Results - Scalability
Chart: 
| Small | Medium | Large | Populous
Resources (slices) | 6927 | 6927 | 7211 | 7474
Increased
PRR Size
Added
PRR
Decreased
PRR Size

## Slide 20: Results - Scalability
Chart: 
| Small | Medium | Large | Populous
Maximum Clock (MHz) | 120.3 | 117.6 | 116.1 | 119.3
All designs
meet 100Mhz constraint

## Slide 21: Conclusions
We developed VAPRES
  Virtual Architecture for Partially Reconfigurable Systems
Contributions
  Modular design methodology
  PR regions with independent, selectable clocks
  Highly parametric design
  Seamless filter swapping
Future work
  Algorithms for runtime module placement
  Tools to assist system design formulation
  Context save and restore for modules

## Slide 22: Thank you for attending
Questions?