## Slide 1: Seamless Hardware Module Swapping for Partially Reconfigurable Stream Processing Systems
Virtual Architecture For Partially Reconfigurable Embedded Systems (VAPRES)
Architecture for creating partially reconfigurable embedded systems
Module communication
Processor – Fast Simplex Links (FSL)
Intermodule – MACS Network on Chip
Highly parametric
  Number of PR regions
  PR region size
  Number of I/O modules
  Independent region clocking
  Module network parameters
Independent development flows
  Applications (HW, SW)
  Base system
  API for run-time reconfiguration
    Module loading
    Seamless filter swapping
    Bitstream relocation
Abelardo Jara-Berrocal, Joseph Antoon, and Ann Gordon-Ross
PR
Region 1
PR
Region 2
PLB Bus
PR Socket
FSL
Switch 1
Switch 2
IF
IF
IF
IF
IO
Module
I/O
MACS
PR Socket
MicroBlaze™ CPU
Control
Seamless Filter Swapping
CPU
Kalman
Filter A
Empty
Region
PR Region 1
PR Region 2
Stage 1 – Preload Filter
Kalman filter A in normal operation
CPU tests Kalman filter A gain
CPU begins loading Kilman filter B
I/O
Module
Target data
CPU
Kalman
Filter A
Empty
Region
PR Region 1
PR Region 2
I/O
Module
Stage 2 –Simultaneous Operation
Filter B is loaded into empty region
End stream word is sent to filter A
Filter A sends state to CPU
PR Region 2
Loading…
Kalman
Filter A
Empty
Region
PR Region 1
PR Region 2
Kalman
Filter B
PR Region 2
Stage 3 – Operation Transfer
CPU initializes filter B
CPU waits for end stream from A
Filter B begins operation
Empty
Region
PR Region 2
Filter B
PR Region 2
Loading…
Kalman
Filter B
PR Region 2
State data
State data
Experimental Setup
End of stream
X
Y
MicroBlaze
IO Module
Camera Interface Image
Decoder
PRR 1
Constant
Gain Kalman
Filter
PRR 2
Variable
Gain
Kalman
Filter
Equipment
Target Ball on cloth backdrop
C3188A Camera Module Omnivision OV7620 sensor 640x480 color 16-bit raw YUV interface
Xilinx ML401 FPGA Board Virtex-4 LX25 FPGA 64MB DDR SDRAM
MACS Interconnect
VAPRES Setup
PR Regions: 2
Basic Kalman filter
Constant gain filter
IO Modules: 1
Camera interface and image recognition
MACS Setup 3 switches 1 channel left and right
Partial Reconfiguration and Adaptation
Systems in harsh, remote regions rely on adaptive behavior
  Power management
  Fault tolerance
  Environmental changes
  Partial reconfiguration helps enable this behavior in reconfigurable systems
  Alters FPGA without interrupting service
  Allows seamless filter swapping, where an old filter functions during reconfiguration
  This prevent critical errors due to reconfiguration downtime
Adaptive Target Tracking
Kalman Filters
  Tracks target from noisy measurements
  Highly parallel calculation ideal for FPGAs
  Different Kalman filters match different targets
Proposed algorithm for adaptive target tracker
  Tracker uses basic Kalman filter at start
  Switches to constant-gain Kalman filter if filter gain does not change over time
  Adaptive clock keeps throughput constant
EJSM
Analysis | Basic | Constant-gain
Max Clock | 156.2 MHz | 71.4 MHz
Throughput | 26 cy / sample | 3 cy / sample
Power | 80.92 mW | 61.18 mW
I/O
Module
CPU
MACS
MACS
MACS
MACS
End stream
Target data
MACS
MACS
Target data
This experiment demonstrates adaptive target tracking of a ball using a camera and near-seamless filter swapping