## Slide 1
Thermal-aware Phase-based Tuning of Embedded Systems
+ Also Affiliated with NSF Center for High-Performance Reconfigurable Computing
This work was supported by National Science Foundation (NSF) grant CNS-0953447
Tosiron Adegbija and Ann Gordon-Ross+
Department of Electrical and Computer Engineering
University of Florida, Gainesville, Florida, USA

## Slide 2: Introduction and Motivation
Embedded systems are ubiquitous with unique design challenges
  Design goals for optimization: reduce cost, energy consumption, time to market, increase performance, etc.
  Design constraints: energy, temperature, area, real-time deadlines, cost, etc.
Temperature is a growing optimization problem
  Embedded systems have few cooling options, usually passive convection
  Increased temperature can lead to increased cooling cost, reduced mean time to failure (MTTF), chip damage, thermal runaway, etc.
Embedded systems must be optimized to manage temperature

## Slide 3: Introduction and Motivation
System optimization is challenging due to numerous tunable parameters
  Tunable parameters: parameters that can be changed
    E.g., cache size, associativity, line size, clock frequency, etc.
  Many combinations  large design space
  Tradeoff design constraints (e.g., temperature)
    Many Pareto optimal designs
Different applications have different parameter value requirements
  Parameter tuning specializes tunable parameters to changing application requirements to meet optimization goals (e.g., lowest energy, best performance)
    Configuration: specific combination of parameter values
    Best configuration: configuration that most closely meets optimization goals
System configuration must not increase peak temperature beyond threshold
  Peak temperature: maximum operating temperature
  Threshold: system temperature constraint
How to tune system configuration to meet temperature goals?
Temperature
Execution time
Pareto
optimal designs

## Slide 4
Dynamic thermal management (DTM) techniques have been proposed
  Clock gating [Brooks ‘01]
    Turn off clock signals during thermal emergencies
  Dynamic voltage scaling (DVS), dynamic frequency scaling (DFS), dynamic voltage and frequency scaling (DVFS) [Skadron‘04]
  Task migration [Heo ‘03]
    Migrate tasks from hot core to cooler core to avoid thermal emergency
DTM may adversely affect other optimization goals
  Must consider Pareto optimal configurations
Application execution characteristics can also affect temperature
  Application characteristics: cache misses, instructions per cycle (IPC), branch mispredictions, etc.
  Considering time-varying intra-application characteristics increases optimization potential
Dynamic Thermal Management
    Phase-based tuning optimizations react to these characteristics
Notes: Figure 1: Average percentage of execution time spent in
corresponding percentage of code size for the top N most
critical code regions, for five MediaBench benchmarks.

## Slide 5
Applications have different phases with different configuration requirements
  A phase is a length of execution where application characteristics (e.g., cache miss rates, branch mispredicts, instructions per cycle, etc.) are relatively stable
Tune when phases change, rather than when applications change
Base energy
Application-based
Time
Energy Consumption
Phase-based
Change configuration
Greater savings when tuning is phase-based,
rather than application-based
Phase-based Tuning
How to determine each phase’s Pareto optimal
configurations to optimize
energy, execution time, and temperature?
Notes: Newer reference?
Figure 1: Average percentage of execution time spent in
corresponding percentage of code size for the top N most
critical code regions, for five MediaBench benchmarks.

## Slide 6: Thermal-aware Phase-based Tuning (TaPT)
We propose TaPT for fine-grained dynamic thermal management (DTM) and phase-based optimization
  Multi-objective optimization problem
    Optimize energy, execution time, and temperature
Combines phase-based cache tuning and DTM
  Cache tuning determines best cache configurations: cache size, line size, and associativity
  Uses dynamic frequency scaling for DTM
Determines Pareto optimal configurations
  Cache configurations and clock frequency
Uses designer-selected priority settings (execution time, energy, temperature)
TaPT is based on Strength Pareto Evolutionary Algorithm II (SPEA2) [Zitzler ‘01]
Notes: Newer reference?
Figure 1: Average percentage of execution time spent in
corresponding percentage of code size for the top N most
critical code regions, for five MediaBench benchmarks.

## Slide 7: Overview of SPEA2 Algorithm
Solution space
Population
Archive
Find non-dominated
solutions
generationi + 1
Pareto optimal solutions
Notes: Newer reference?
Figure 1: Average percentage of execution time spent in
corresponding percentage of code size for the top N most
critical code regions, for five MediaBench benchmarks.

## Slide 8: TaPT Algorithm
For each new phase Random subset of configuration space
Designer-specified priority settings: X, execution time; N, energy; T, temperature
Start: Generate population, P
Notes: Newer reference?
Figure 1: Average percentage of execution time spent in
corresponding percentage of code size for the top N most
critical code regions, for five MediaBench benchmarks.

## Slide 9: TaPT Algorithm
Designer-specified priority settings: X, execution time; N, energy; T, temperature
Start: Generate population, P
Determine most similar phase’s archive, Amsp
Set current phase’s archive, A to Amsp
Amsp ← archive(Pj) | D = min(Dj)
Dj ← d(Pi, Pj)
Notes: Newer reference?
Figure 1: Average percentage of execution time spent in
corresponding percentage of code size for the top N most
critical code regions, for five MediaBench benchmarks.

## Slide 10: TaPT Algorithm
Designer-specified priority settings: X, execution time; N, energy; T, temperature
Start: Generate population, P
Determine most similar phase’s archive, Amsp
Set current phase’s archive, A to Amsp
Calculate fitness of individuals in P U A
Update archive with non-dominated individuals
Final generation?
Determine best configuration from archive
Yes
No
Return to start
Strength, S(Ci) = |{Cj | Cj ϵ P U A Ci ≻ Cj}|
Fitness, R(Ci) = ƩS(Cj) ∀ Cj ϵ P U A, Cj ≻ Ci
Cj is non-dominated if R(Cj) = 0
Notes: Newer reference?
Figure 1: Average percentage of execution time spent in
corresponding percentage of code size for the top N most
critical code regions, for five MediaBench benchmarks.

## Slide 11: Experimental Setup
Modeled ARM Cortex A9
  Level 1 (L1) instruction and data caches: cache size (8kB 32kB); line size (16B64B); associativity (direct-mapped4-way)
  Clock frequency: 800 MHz to 2 GHz
    200 MHz increments
  Base cache configuration:
    L1 instruction and data caches: cache size (32kB); line size (64B); associativity (4-way); 2 GHz clock frequency
18 benchmarks from EEMBC and Mibench suites
  Specific compute kernels
    E.g., JPEG compression and decompression, audio encoding and decoding, networking, etc.
  Each workload represented a phase

## Slide 12: Experimental Setup
Simulations
  GEM5 generated cache miss rates
  McPAT calculated power consumption
    Energy delay product (EDP)
      = system_power * (total_phase_cycles/system_frequency)2
  Hotspot for thermal modeling
    4 K/W convection resistance, 1 mm heat sink thickness, 0.1 mm spreader thickness
TaPT parameters
  Population size: 20
  Number of generations: 3
  Archive size: 5
  Balance between Pareto optimal solutions and tuning overhead
    Evaluates only 4% of design space

## Slide 13: Results
Chart: Execution time, energy, EDP, temperature normalied to the base configuration
| sha | patricia | dijkstra | djpeg | cjpeg | mad | ttsprk01 | tblook01 | rspeed01 | puwmod01 | pntrch01 | iirflt01 | canrdr01 | cacheb01 | bitmnp01 | basefp01 | aifftr01 | a2time01 | average
Execution time | 1.0086 | 1.0113 | 1.1386 | 1.0323 | 1.041 | 1.0562 | 0.93372 | 1.0018 | 0.7493 | 0.82455 | 1.0016 | 1.0031 | 0.82007 | 0.98054 | 0.89975 | 0.90935 | 0.83218 | 1.0004 | 0.95802
Energy | 0.70429 | 0.85063 | 0.80433 | 0.72684 | 0.70643 | 0.75245 | 0.63438 | 0.70443 | 0.66011 | 0.5784 | 0.69762 | 0.6956 | 0.57243 | 0.67817 | 0.65923 | 0.64351 | 0.58701 | 0.71298 | 0.68716
EDP | 0.71033 | 0.86022 | 0.91583 | 0.75033 | 0.7354 | 0.79475 | 0.59233 | 0.70567 | 0.49462 | 0.47692 | 0.69871 | 0.69776 | 0.46943 | 0.66497 | 0.59314 | 0.58517 | 0.4885 | 0.71323 | 0.66374
Temperature | 0.7754 | 0.915 | 0.78067 | 0.77977 | 0.76839 | 0.78489 | 0.76898 | 0.77955 | 0.91472 | 0.77808 | 0.77592 | 0.77385 | 0.77491 | 0.77329 | 0.79994 | 0.78153 | 0.77977 | 0.78515 | 0.79388
Priority N (energy prioritization)
  Temperature threshold: 82oC
  Average execution time, energy, EDP, and temperature savings of 4%, 31%, 34%, and 20%, respectively.
Zero designer effort: no specified priority
    Temperature threshold: 82oC
  Average execution time, energy, EDP, and temperature savings of 2%, 30%, 31%, and 21%, respectively.
Chart: Execution time, energy, EDP, temperature normalized to the base configuration
| sha | patricia | dijkstra | djpeg | cjpeg | mad | ttsprk01 | tblook01 | rspeed01 | puwmod01 | pntrch01 | iirflt01 | canrdr01 | cacheb01 | bitmnp01 | basefp01 | aifftr01 | a2time01 | average
Execution time | 1.0017 | 0.99753 | 1.0557 | 1.0104 | 1.0274 | 1.042 | 0.95752 | 1.0051 | 1.0001 | 1.0032 | 0.86163 | 1.0023 | 0.81206 | 0.97919 | 0.89953 | 1.0033 | 1.05 | 0.99804 | 0.98371
Energy | 0.70717 | 0.87674 | 0.73779 | 0.7298 | 0.73983 | 0.74156 | 0.65149 | 0.64361 | 0.63325 | 0.69387 | 0.60666 | 0.7035 | 0.72566 | 0.67877 | 0.66509 | 0.69314 | 0.7393 | 0.67079 | 0.70211
EDP | 0.70841 | 0.87457 | 0.7789 | 0.7374 | 0.76012 | 0.77267 | 0.62381 | 0.64687 | 0.63333 | 0.69612 | 0.52271 | 0.70514 | 0.58928 | 0.66464 | 0.59827 | 0.69544 | 0.77627 | 0.66947 | 0.69186
Temperature | 0.78031 | 0.9308 | 0.77602 | 0.79182 | 0.7906 | 0.78514 | 0.76964 | 0.7488 | 0.74361 | 0.77174 | 0.78043 | 0.77799 | 0.92782 | 0.77476 | 0.80379 | 0.77186 | 0.77923 | 0.76475 | 0.79273

## Slide 14: Results
Chart: Execution time, energy, EDP, temperature normalized to the base configuration
| sha | patricia | dijkstra | djpeg | cjpeg | mad | ttsprk01 | tblook01 | rspeed01 | puwmod01 | pntrch01 | iirflt01 | canrdr01 | cacheb01 | bitmnp01 | basefp01 | aifftr01 | a2time01 | average
Execution time | 1.5618 | 1.1595 | 1.3728 | 1.2971 | 1.2827 | 1.703 | 1.4314 | 1.4289 | 1.4292 | 1.2507 | 1.4297 | 1.1169 | 1.4836 | 1.4309 | 1.2844 | 1.43 | 1.4577 | 1.429 | 1.3877
Energy | 0.9575 | 0.87315 | 0.90115 | 0.79588 | 0.83097 | 1.0441 | 0.86489 | 0.88578 | 0.86351 | 0.81027 | 0.8772 | 0.73655 | 0.89767 | 0.86449 | 0.82208 | 0.87741 | 0.89443 | 0.87679 | 0.87077
EDP | 1.4954 | 1.0124 | 1.2371 | 1.0324 | 1.0659 | 1.7781 | 1.238 | 1.2657 | 1.2342 | 1.0134 | 1.2541 | 0.82267 | 1.3318 | 1.237 | 1.0559 | 1.2547 | 1.3039 | 1.2529 | 1.2159
Temperature | 0.73296 | 0.87538 | 0.75306 | 0.73416 | 0.75426 | 0.73358 | 0.73028 | 0.74008 | 0.73007 | 0.75345 | 0.73535 | 0.75628 | 0.73022 | 0.73138 | 0.75677 | 0.73479 | 0.73473 | 0.73479 | 0.74731
Priority T (temperature prioritization): 65oC temperature threshold
  Average energy and temperature savings of 13% and 25%, respectively
  Average execution time and EDP increases of 39% and 22%, respectively
Chart: Execution time, energy, EDP, temperature normalized to base configuration
| sha | patricia | dijkstra | djpeg | cjpeg | mad | ttsprk01 | tblook01 | rspeed01 | puwmod01 | pntrch01 | iirflt01 | canrdr01 | cacheb01 | bitmnp01 | basefp01 | aifftr01 | a2time01 | average
Execution time | 1.0011 | 0.96505 | 1.0478 | 1.0107 | 1.0169 | 1.0514 | 0.84565 | 0.75652 | 1 | 1.001 | 0.98453 | 0.79833 | 1.0003 | 0.97919 | 0.89909 | 0.9111 | 1.0031 | 0.88531 | 0.95317
Energy | 0.89546 | 0.85294 | 0.92183 | 0.72901 | 0.73722 | 0.64242 | 0.59067 | 0.52985 | 1 | 0.70664 | 0.66899 | 0.53081 | 0.83157 | 0.68854 | 0.92942 | 0.64957 | 0.82751 | 0.6418 | 0.74302
EDP | 0.89642 | 0.82313 | 0.9659 | 0.73679 | 0.74971 | 0.67547 | 0.49949 | 0.40085 | 1 | 0.70735 | 0.65864 | 0.42376 | 0.83183 | 0.67421 | 0.83563 | 0.59183 | 0.83004 | 0.5682 | 0.71496
Temperature | 0.92131 | 0.93383 | 0.91504 | 0.79106 | 0.79092 | 0.73361 | 0.77575 | 0.77702 | 1 | 0.78065 | 0.76975 | 0.75927 | 0.86288 | 0.78056 | 1.0204 | 0.78654 | 0.86619 | 0.79146 | 0.83646
Priority X (execution time prioritization)
  Average execution time, energy, EDP, and temperature savings of 5%, 26%, 29%, and 16%, respectively.
Stringent temperature constraint
negatively impacts other optimization
goals!
TaPT adheres to design constraints and specified priority settings!

## Slide 15: Conclusions
We introduced thermal-aware phase-based tuning (TaPT) for embedded systems
  Combines phase-based cache tuning and dynamic thermal management (DTM)
  Simultaneously optimize for execution time, energy, and temperature
    Multi-objective optimization
  Determined Pareto optimal configurations
  Adhered to specified design constraints
  Up to 5%, 30%, and 25% execution time, energy, and temperature savings, respectively
  Effectively traded off non-prioritized constraints
    E.g., Increase execution time for tight temperature constraints
Future work
  Incorporate phase classification into TaPT algorithm
  Verify TaPT’s scalability to more complex systems and larger design spaces
Notes: Newer reference?
Figure 1: Average percentage of execution time spent in
corresponding percentage of code size for the top N most
critical code regions, for five MediaBench benchmarks.

## Slide 16: Questions?