## Slide 1
Markov Modeling of Fault-Tolerant
Wireless Sensor Networks
Arslan Munir and Ann Gordon-Ross+
Department of Electrical and Computer Engineering
University of Florida, Gainesville, Florida, USA
This work was supported by the Natural Sciences and Engineering Research Council of Canada (NSERC)
+ Also affiliated with NSF Center for High-Performance Reconfigurable Computing

## Slide 2: Wireless Sensor Networks (WSNs)
WSN
Applications
Security and
Defense Systems
Health Care
Ambient conditions
Monitoring, e.g. ,
forest fire detection
Industrial
Automation
Logistics
Ever Increasing

## Slide 3: WSN Design Challenges
WSN
Design
Challenges
Meeting application requirements
e.g., reliability, lifetime, throughput,
delay (responsiveness), etc.
Application requirements
change over time
Environmental conditions (stimuli)
change over time
Failure to meet
Catastrophic
Consequences
Forest fire could spread
uncontrollably in the
case of a forest fire
detection application
Loss of life in the case
of health care application
Major disasters in the
case of defense systems

## Slide 4: WSN Hierarchical View
Lifetime
Reliability
MTTF
Application
Requirements
Gateway
Sensor
Nodes
WSN
Cluster
WSN
Cluster
Head
Sink
Node
Computer
Network
WSN
Designer
Sensor
Field
Average time to
WSN failure

## Slide 5: WSN Fault-Detection and Fault-Tolerance
WSN
Fault-detection &
Fault-tolerance
Fault-detection => Distributed fault-detection (DFD) algorithms
that identify faulty sensor readings to indicate sensor faults
Necessity
Sensor nodes deployed in unattended and
hostile environments => susceptible to failures
Manual inspection of faulty sensor nodes
after deployment is impractical
Many WSN applications are mission critical
and require continuous operation
DFD algorithm’s accuracy =>
Algorithm’s ability to accurately
identify faults
Fault-tolerance => Adding hardware/software
redundancy to the system

## Slide 6: WSN Fault-Tolerance
WSN
Fault-tolerance
Fault-tolerance => Adding hardware/software
redundancy to the system
Where to add redundancy?
Within a sensor node
Within a cluster => redundant sensor nodes
Within a WSN => redundant WSN clusters
Sensors (e.g., temperature and
humidity sensors) have higher
failure rates than other components
(e.g., processors, transceivers, etc.)
Sensors are cheap =>
Adding spare sensors
contribute little to a
sensor node’s cost

## Slide 7: Contributions
Investigate synergy between
fault-detection and
fault-tolerance (FT) for WSNs
Fault-tolerance for
WSNs
Develop a Markov model for characterizing
WSN reliability and MTTF
Proposed a duplex sensor node
model for fault-tolerance
Helps WSN designer in determining
the exact number of sensor nodes
required to meet the application’s
lifetime and reliability requirements
Provides an insight into the type of
sensor nodes (duplex or simplex)
feasible for an application to meet
the application’s requirements
A good DFD
algorithm is necessary
for robust FT
Used a hierarchical approach =>
WSN Markov model leverages
WSN cluster model
which in turn leverages
sensor node model

## Slide 8: NFT and FT Sensor Node Markov Model
0
1
2
0
1
Non-fault-tolerant (NFT) Sensor Node Markov Model
Fault-tolerant (FT) Sensor Node Markov Model
= Sensor failure rate
C = Coverage factor
Probability that the faulty sensor
is correctly diagnosed, disconnected,
and replaced by a good inactive
spare sensor
Failed State
Failed State
1 Non-Faulty
Sensor
2 Non-Faulty
Sensors
Proposed Duplex
Model

## Slide 9: FT Sensor Node Markov Model – Differential Equation Solutions
Reliability
  where
  Pi (t) = Probability that sensor node will be in state i at time t
MTTF
Average Failure Rate (or Failures in Time (FIT))
  where
  k denotes the average number of sensor node neighbors
  k is important as DFD algorithm’s accuracy depends upon k

## Slide 10: FT WSN Cluster Model
kmin+1
n
n-1
kmin
kmin+1
kmin
kmin+2
Average number
of nodes in each cluster is n
Average number of
neighbor nodes per cluster
is k = n - 1
We consider a special case with n = kmin+2
A cluster fails to
perform its assigned
application task if the
number of non-faulty
sensor nodes in the
cluster reduces to kmin

## Slide 11: FT WSN Cluster Markov Model – Differential Equation Solutions (n = kmin+2)
Reliability
MTTF

## Slide 12: FT WSN Cluster Markov Model – Differential Equation Solutions (n = kmin+2)
Average Failure Rate
  where
  MTTFc(n) denotes the MTTF of a WSN cluster of n sensor nodes
Sensor
Nodes
WSN
Cluster
WSN
Cluster
Head
Sink
Node
Sensor
Field

## Slide 13: FT WSN Model
Nmin+1
N
N-1
Nmin
λc(n) corresponds to
the failure rate of a WSN
cluster with n sensor nodes
  where
  ns denotes the total number of sensor nodes in the WSN
  n denotes the average number of nodes in a cluster
A typical WSN consists of N = ns/n clusters
WSN fails to perform
its assigned task when
the number of alive
clusters reduces to Nmin

## Slide 14: FT WSN Markov Model – Differential Equation Solutions (N = Nmin+2)
Reliability
MTTF

## Slide 15: Experimental Results
SHARPE Software Package
  Markov model implementations
    NFT sensor node
    FT sensor node
    NFT WSN cluster
    FT WSN cluster
    NFT WSN
    FT WSN
Sensor Failure Probability
  Exponential distribution
  where
  p = sensor failure probability
  λs = sensor failure rate over period ts
  ts = time over which sensor failure probability/failure rate is specified
  We present results for ts = 100 days
Sensor
Nodes
WSN
Cluster
WSN
Cluster
Head
Sink
Node
Sensor
Field
Our Markov models
are valid for any other
distribution as well

## Slide 16: Results – MTTF FT & NFT Sensor Nodes
MTTF (days) for an FT and a non-FT (NFT) sensor node.
c = coverage factor
k = number of neighbor
sensor nodes
c = 1 for an ideal
DFD algorithm and
an ideal replacement of
faulty sensor with a
non-faulty sensor
An FT sensor node has a remarkable difference in MTTF as compared to an NFT sensor node: approx 95% improvement!!
c improves as the number of neighboring sensor nodes k increases (DFD specifics) and hence the MTTF for an FT sensor node increases
MTTF for both NFT and FT sensor node decreases as p increases

## Slide 17: Results – Reliability FT & NFT Sensor Node
Reliability for an NFT and an sensor node
p | NFT | FT (k=5, c≠1) | FT (k=10, c≠1) | FT (c=1)
0.05 | 0.94999 | 0.99770 | 0.99872 | 0.99872
0.1 | 0.89996 | 0.98135 | 0.99074 | 0.99482
0.2 | 0.80011 | 0.93481 | 0.95088 | 0.97853
0.3 | 0.69977 | 0.86265 | 0.88263 | 0.94959
0.4 | 0.59989 | 0.77094 | 0.79209 | 0.90643
0.5 | 0.5007 | 0.66086 | 0.68097 | 0.84662
0.6 | 0.40012 | 0.53610 | 0.55295 | 0.76663
0.7 | 0.30119 | 0.40167 | 0.41432 | 0.66262
0.8 | 0.19989 | 0.25943 | 0.26683 | 0.52171
0.9 | 0.10026 | 0.12148 | 0.12424 | 0.33086
0.99 | 0.01005 | 0.01048 | 0.01053 | 0.05628
The percentage
improvement
in reliability for an
FT sensor node with
c=1 over an NFT sensor
node and FT sensor node
with c≠1 and k = 5 and 10
is 230%, 172%, and
166%, respectively
for p=0.9
The percentage
improvement in
reliability attained
by an FT sensor node
with c = 1 increases
as p →1 because
because for an FT
sensor node with
c≠1, c decreases
as p →1
(DFD specifics)
230%
172%
166%

## Slide 18: Results – MTTF FT & NFT WSN Cluster
MTTF (days) for the FT and non-FT (NFT) WSN clusters with kmin = 4.
MTTF for FT WSN clusters with c=1 is always better than the FT WSN clusters with c≠1
The FT WSN cluster with n=kmin+5 has more redundant senor nodes as compared to the FT WSN cluster with n=kmin+2 and thus has a comparatively greater MTTF
MTTF for both NFT and FT WSN cluster decreases as p increases

## Slide 19: Results – Reliability FT & NFT WSN Cluster
Reliability for an NFT and an FT WSN cluster when n = kmin + 2 (kmin= 4)
p | NFT | FT (c≠1) | FT (c=1)
0.05 | 0.96720 | 0.99058 | 0.99098
0.1 | 0.88562 | 0.95969 | 0.96552
0.2 | 0.65567 | 0.84304 | 0.87474
0.3 | 0.41968 | 0.66438 | 0.74422
0.4 | 0.23309 | 0.45925 | 0.59388
0.5 | 0.10942 | 0.26595 | 0.43653
0.6 | 0.04098 | 0.11837 | 0.28732
0.7 | 0.01114 | 0.03548 | 0.16279
0.8 | 0.0015957 | 0.0043470 | 0.06723
0.9 | 5.5702x10-5 | 1.4838x10-4 | 0.01772
0.99 | 6.1056x10-10 | 1.0057x10-9 | 5.5702x10-5
The percentage
improvement
in reliability for an
FT WSN cluster with
c=1 over an NFT WSN
cluster and FT WSN
cluster with c≠1
is 601% and 143%,
respectively for p=0.6
601%
143%

## Slide 20: Results – MTTF FT & NFT WSN
MTTF (days) for the FT and non-FT (NFT) WSNs with Nmin = 0.
MTTF percentage
improvement for FT WSN over NFT WSN
is 88% for p=0.1
MTTF for WSNs with N=Nmin+5
is always greater than the MTTF for WSNs with N=Nmin+2
(due to additional redundancy
in WSN with N=Nmin+5)
MTTF percentage improvement
for FT WSN over NFT WSN
drops to 3.3% for p=0.99
Low failure
probability sensors
are required to build
a more reliable
FT WSN

## Slide 21: Results – Reliability FT & NFT WSN
Reliability for an NFT and FT WSN when N = Nmin+ 2 (Nmin = 0)
p | NFT | FT (c≠1) | FT (c=1)
0.05 | 0.99557 | 0.99883 | 0.99885
0.1 | 0.98261 | 0.99474 | 0.99534
0.2 | 0.93321 | 0.97583 | 0.98084
0.3 | 0.85557 | 0.93775 | 0.95482
0.4 | 0.75408 | 0.87466 | 0.91611
0.5 | 0.63536 | 0.78202 | 0.86218
0.6 | 0.51166 | 0.65121 | 0.78948
0.7 | 0.36303 | 0.49093 | 0.69527
0.8 | 0.20933 | 0.30328 | 0.55494
0.9 | 0.08807 | 0.11792 | 0.39647
0.99 | 0.004054 | 0.004952 | 0.08807
An FT WSN can
deliver much better
reliability than an
NFT WSN even for
higher sensor failure
probability p
The percentage
improvement
in reliability for an
FT WSN with c=1
over an NFT WSN
and FT WSN with c≠1
is 350% and 236%,
respectively for p=0.9
350%
236%

## Slide 22: Conclusions
We proposed an FT duplex sensor node model
  A novel concept for determining the coverage factor using sensor fault detection algorithm accuracy
We developed hierarchical Markov models for WSNs consisting of sensor node clusters to compare the MTTF and reliability for FT and NFT WSNs
  Aids design of WSNs with different lifetime and reliability requirements
Fault detection algorithm’s accuracy plays a critical role in FT WSNs
FT duplex sensor node provides improvement over an NFT sensor node
  100% MTTF improvement with a perfect fault detection algorithm (c = 1)
  MTTF improvement from 96% for current fault detection algorithms with low p
  (p < 0.3) - MTTF improvement reduces to 1.3% as p → 1
Percentage reliability improvement for an FT WSN with c = 1 over an NFT WSN with c≠1 is 350% and over an FT WSN with c≠1 is 236% for p=0.9
Redundancy in WSN plays an important role in improving MTTF
  Our models allow designers to determine the fault detection algorithm’s accuracy and required redundancy to meet application requirements