## Slide 1
CPACT –
The Conditional Parameter Adjustment
Cache Tuner for Dual-Core Architectures
+ Also Affiliated with NSF Center for High-Performance Reconfigurable Computing
Marisha Rawlins and Ann Gordon-Ross+
University of Florida Department of Electrical and Computer Engineering
This work was supported by National Science Foundation (NSF) grant CNS-0953447

## Slide 2: Introduction
Design space
100’s – 10,000’s
Power hungry caches are a good candidate for optimization
Different applications have vastly different cache parameter value requirements
  Configurable parameters: size, line size, associativity
  Parameter values that do not match an application’s needs can waste over 60% of energy (Gordon-Ross ‘05)
Cache tuning determines appropriate cache parameters values (cache configuration) to meet optimization goals (e.g., lowest energy)
However, highly configurable caches can have very large design spaces (e.g., 100s to 10,000s)
  Efficient heuristics are needed to efficiently search the design space
Lowest energy

## Slide 3: Introduction
Power hungry caches are a good candidate for optimization
Different applications have vastly different cache requirements
  Cache parameters that do not match an application’s needs can waste over 60% of energy (Gordon-Ross ‘05)
Cache tuning determines appropriate cache parameters (cache configuration) to meet optimization goals (e.g., lowest energy)
  Configurable parameters include: size, line size, associativity
L1 Data Cache
32KB, 2-way,
32B linesize
Application 2
Application 1
L1 DataCache
16KB, direct-mapped,
16B line size
Application 3
L1 Data Cache
64KB, 4-way,
64B linesize
Lowest Energy Cache Configuration
Configurable cache is required to provide this specialization

## Slide 4: Configurable Cache Architecture
Configurable caches enable cache tuning
  Specialized hardware enables the cache to be configured at startup or in system during runtime
2KB
2KB
2KB
2KB
8 KB, 4-way base cache
2KB
2KB
2KB
2KB
8 KB, 2-way
2KB
2KB
2KB
2KB
8 KB, direct-mapped
Way concatenation
2KB
2KB
2KB
2KB
4 KB, 2-way
2KB
2KB
2KB
2KB
2 KB, direct-mapped
Way shutdown
Configurable Line size
16 byte physical line size
A Highly Configurable Cache (Zhang ‘03)
Tunable Asociativity
Tunable Size
Tunable Line Size

## Slide 5: Runtime Cache Tuning
Optimal configuration typically determined by executing application in each configuration for a period of time
  Chooses the lowest energy configuration
  Executes non-optimal, higher energy configurations
  Energy overhead
Choose lowest energy configuration
Possible Cache Configurations
Energy
Time
Energy
System startup
Cache tuning
Exhaustive exploration can unnecessarily expand this high energy tuning time
Energy Overhead

## Slide 6: Runtime Tuning Challenges
Heuristic tuning method
Design space
100’s – 10,000’s
Lowest energy
Searches fewer configurations
Possible Cache Configurations
Energy
Exhaustive method
Possible Cache Configurations
Energy
Heuristic method
Reduces tuning energy overhead
System Startup
Energy
Exhaustive method
System Startup
Energy
Heuristic method
Cache tuning heuristics have been developed for single-core systems to reduce the exploration and tuning overhead

## Slide 7: Previous Tuning Heuristics
Microprocessor
Main Memory
I$
D$
Tuner
Zhang’s Configurable Cache
18 configurations per cache
Independently tuned
L1
Microprocessor
Main Memory
I$
D$
Tuner
I$
D$
Two Level Configurable Cache
216 configurations per cache hierarchy
L1
L2
Dependency Any L1 change affects what and how many addresses stored L2
Single Level Energy-Impact-Ordered Cache Tuning (Zhang ‘03)
Increase Size
Increase Line Size
Increase Associativity
2. Search each parameter in order from smallest to largest
3. Stop searching a parameter when increase in energy
1. Initialize each parameter to smallest value
Notes: Need to mention motivation for heuristics. Doesn’t have to be in this slide, but should be at least mentioned before this slide.
Also, for this slide and the next there should be animations in my presentations you can use. Make sure you check my talks section on my pubs page because my PhD defense should have it (the “hot caches, cool techniques” talk).

## Slide 8: Previous Tuning Heuristics
Microprocessor
Main Memory
I$
D$
Tuner
Zhang’s Configurable Cache
18 configurations per cache
Independently tuned
L1
Microprocessor
Main Memory
I$
D$
Tuner
I$
D$
Two Level Configurable Cache
216 configurations per cache hierarchy
L1
L2
Tuning dependency
40% energy savings
Single Level Impact Ordered Cache Tuning (Zhang ‘03)
Increase Size
Increase Line Size
Increase Associativity
Impact Order
Continue increasing parameter as long as the increase results in a decrease in energy consumption
Tune instruction cache
Tune data cache
Decrease Energy Consumption?
Notes: Need to mention motivation for heuristics. Doesn’t have to be in this slide, but should be at least mentioned before this slide.
Also, for this slide and the next there should be animations in my presentations you can use. Make sure you check my talks section on my pubs page because my PhD defense should have it (the “hot caches, cool techniques” talk).

## Slide 9: Level One and Level Two Dependencies
Processor needs:
EFGH
ABCD
I
JKL
UVWX
A B C D
E F G H
I J K L
E F G H
M N O P
QRST
L1 cache
EFGH
ABCD
L2 cache
EFGH
I
JKL
MNOP
ABCD
L1 cache
ABCD
L2 cache
EFGH
I
JKL
MNOP
Replace L1 &
update L2
EFGH
I
JKL
Increase L1 size?
from memory
EFGH
MNOP
I
JKL
ABCD
EFGH
--  L1 size,  L1 hits,  energy savings
-- Can we use a smaller, lower energy L2
cache?
-- How small can we make the L2 cache
and still achieve energy savings?
direct-
mapped
2-way associative
EFGH
Increase L1 associativity
--  L1 associativity,  L1 hits,  energy savings
-- Changes the values in L2 cache
-- Changes the performance and energy
consumption of the L2 cache
-- Increase L2 size or associativity?
L1
L2
Tuning dependency

## Slide 10: The Two Level Cache Tuner (TCaT)
Microprocessor
Main Memory
I$
D$
Tuner
I$
D$
L1
L2
1. Tune L1 Size
I$
I$
2. Tune L2 Size
I$
3. Tune L1 Line Size
I$
4. Tune L2 Line Size
I$
5. Tune L1 Associativity
I$
6. Tune L2 Associativity
Do the same for the data cache hierarchy
(Gordon-Ross ’04)
Alternating Cache Exploration with Additive Way Tuning (ACE-AWT)
(Gordon-Ross ’05)
Microprocessor
Main Memory
I$
D$
Tuner
U$
We learned from previous work:
-- Order of parameter tuning
-- Must consider tuning
dependencies when tuning
multiple caches

## Slide 11: The Two Level Cache Tuner (TCaT)
The two levels should not be explored separately
  L2 cache performance depends on misses in the L1 cache
To more fully explore the dependencies between the two levels, interleave the exploration of the level one and level two caches
Achieved 53% energy savings
Searched 6.5% of the design space
Microprocessor
Main Memory
I$
D$
Tuner
I$
D$
L1
L2
1. Tune L1 Size
I$
I$
2. Tune L2 Size
I$
3. Tune L1 Line Size
I$
4. Tune L2 Line Size
I$
5. Tune L1 Associativity
I$
6. Tune L2 Associativity
Do the same for the data cache hierarchy
(Gordon-Ross ’04)

## Slide 12: Alternating Cache Exploration with Additive Way Tuning (ACE-AWT)
Extended TCaT for a unified second level cache
  More complex interdependency to consider
  Interleaved L1 and L2 tuning
A change in any cache affects the performance of all other caches in the hierarchy
Microprocessor
Main Memory
I$
D$
Tuner
U$
Achieved 62% energy savings
Searched 0.2% of the design space
(Gordon-Ross ’05)
We learned from previous work:
-- Order of parameter tuning
-- Must consider tuning
dependencies when tuning
multiple caches

## Slide 13: Motivation
Explore multi-core optimizations
  Meet power, energy, performance constraints
Multi-core optimization challenges with respect to single-core
  Not just a single core to optimize
  Must consider task-to-core allocation and per-core requirements
    Each core assigned disjoint tasks/processes
    Each core assigned subtask of single application
  Maximum savings  heterogeneous core configurations
Apply lessons learned in single-core optimizations
  Practical adaptation is non-trivial
   design space size
  New multi-core-specific dependencies to consider
    Core interactions
    Data sharing
    Shared resources
Notes: I’ll probably get rid of this slide

## Slide 14: Multi-core Challenges
Design Space
Design Space
P0
8KB, 4-way,
16B line size
P2
2KB, 1-way,
64B line size
P3
8KB, 2-way,
32B line size
P4
64KB, 4-way,
64B line size
P5
32KB, 1-way,
16B line size
P6
4KB, 1-way,
32B line size
P7
16KB, 2-way,
32B line size
Allow heterogeneous cores –
each core’s cache can have a different configuration
lowest energy
cache configuration
for each core
P1
16KB, 2-way,
32B line size
Number of configurations to explore grows exponentially with the number of processors
App
P0
P1
P2
P3
P4
P5
P6
P7
Processors:

## Slide 15: Multi-core Challenges
Design Space
Design Space
P0
8KB, 4-way,
16B line size
P1
8KB, 4-way,
16B line size
P2
2KB, 1-way,
64B line size
P3
8KB, 2-way,
32B line size
P4
64KB, 4-way,
64B line size
P5
32KB, 1-way,
16B line size
P6
4KB, 1-way,
32B line size
P7
16KB, 2-way,
32B line size
Allow heterogeneous cores –
each core’s cache can have a different configuration
lowest energy
cache configuration
for each core
P1
16KB, 2-way,
32B line size
Number of configurations to explore grows exponentially with the number of processors
App
P0
P1
P2
P3
P4
P5
P6
P7
Processors:

## Slide 16: Multi-core Challenges
Design Space
Design Space
P0
8KB, 4-way,
16B line size
P1
8KB, 4-way,
16B line size
P2
2KB, 1-way,
64B line size
P3
8KB, 2-way,
32B line size
P4
64KB, 4-way,
64B line size
P5
32KB, 1-way,
16B line size
P6
4KB, 1-way,
32B line size
P7
16KB, 2-way,
32B line size
Allow heterogeneous cores –
each core’s cache can have a different configuration
lowest energy
cache configuration
for each core
P1
16KB, 2-way,
32B line size
Number of configurations to explore grows exponentially with the number of processors
Increase energy savings?
App
P0
P1
P2
P3
P4
P5
P6
P7
Processors:

## Slide 17: Multi-core Challenges
Data Sharing
A B C D
E F G H
I J K L
E F G H
ABCD
ABCD
EFGH
ABCD
EFGH
I
JKL
Hit
Miss
Hit
Miss
Hit
Miss
Hit
Miss
P0
 miss rate
high energy misses
 Energy Savings
P1
E F G H
XXXX
Invalidate
Coherence Miss in P0
 cache size ≠  cache misses
P0
P1
Shared Data
In which order can we tune the caches?
Can the caches be tuned separately?
I need…
d-cache
d-cache
d-cache
Increase
d-cache size
I’m updating…
Invalidating …
Results in a cache:

## Slide 18: Contribution
We quantify level one data cache tuning energy savings in a dual-core system
  Heterogeneous cache configurations with configurable total size, line size, and associativity
Conditional Parameter Adjustment Cache Tuner (CPACT)
  Cache tuning heuristic for lowest energy cache configuration
    24% average energy savings for the level one data caches
    Searches only 1% of the design space
Analyze the data sharing and core interactions of our applications

## Slide 19: CPACT Heuristic and Results

## Slide 20: Experimental Setup
SESC1 simulator provided cache statistics
11 applications from the SPLASH-22 multithreaded suite
Design space:
  36 configurations per core
    L1 data cache size: 8KB, 16KB, 32KB, 64KB
    L1 data cache line size: 16 bytes, 32 bytes, and 64 bytes
    L1 data cache associativity: 1-, 2-, and 4-way associative
  1,296 configurations for a dual-core heterogeneous system
Energy model
  Based on access and miss statistics (SESC) and energy values (CACTIv6.53)
  Calculated dynamic, static, cache fill, write back, CPU stall energy
  Includes energy and performance tuning overhead
Energy savings calculated with respect to our base system
  Each data cache set to a 64kB, 4-way associative, 64 byte line size L1 cache
1 (Ortego/Sack 04), 2(Woo/Ohara 95), 3(Muralimanohar/Jouppi 09)

## Slide 21: Dual-core Optimal Energy Savings
Optimal lowest energy configuration found via an exhaustive search
Some applications required heterogeneous configurations
Chart: Energy Savings (%)
| cholesky | fft | lucon | lunon | ocean-con | ocean-non | radiosity | radix | raytrace | water-nsquared | water-spatial | Avg
dual core (optimal) | 0.095185 | 0.18022 | 0.37447 | 0.2115 | 0.14394 | 0.014434 | 0.50195 | 0.32 | 0.26698 | 0.19081 | 0.44321 | 0.25498
25%
50%
L1 data cache tuning

## Slide 22: CPACT
The Conditional Parameter Adjustment Cache Tuner
Initial Impact Ordered Tuning
(Zhang ‘03)
Size Adjustment
Final Parameter Adjustment
$ Tuner
$ Tuner
Micro-
processor
L1 Data Cache
Main Memory
Instruction Cache
Micro-
processor
L1 Data Cache
Instruction Cache
shared signal
-- Both processors tune
simultaneously
-- Both processors must start each
tuning step at the same time
Coordinate tuning:
P0
P1
P0 & P1 both start impact ordered tuning
P0_initial
P0_Cfg0
P1_Cfg0
P0_Cfg1
P1_Cfg1
P1_Cfg2
Stay in P0_initial
P1_initial
P1_Cfg4
P1_Cfg3
P0 & P1 both start size adjustment
WAIT?
Results showed that this coordination is critical for applications with high data sharing

## Slide 23: CPACT- Initial Impact Ordered Tuning
For each L1 data cache:
first tune the cache size
Start with 8KB, direct-mapped,
16 byte
Current L1 cfg
Evaluate
cmp
energy
decrease in energy
increase in energy
or reached largest size
Tune line size
Tune associativity
WAIT?
Equivalent to applying single-core L1 cache tuning heuristic on each core
Only 1% average energy savings
Initial Cfg

## Slide 24
CPACT- Initial Impact Ordered Tuning
benchmark | after initial tuning
 | %diff
cholesky | 11%
fft | 6%
lucon | 15%
lunon | 26%
ocean-con | 0%
ocean-non | 2%
radiosity | 22%
radix | 1%
raytrace | 22%
water-nsquared | 0%
water-spatial | 0%
Avg | 10%
% difference between energy consumed by initial configuration and optimal
Single-core L1 cache tuning heuristic not sufficient for finding optimal
Next we adjust the cache size again
Initial Impact Ordered Tuning
Size Adjustment
Final Parameter Adjustment

## Slide 25
CPACT- Size Adjustment
Initial Impact Ordered Tuning
Size Adjustment
Final Parameter Adjustment
benchmark | after initial tuning | after size adjustment
 | %diff | % diff
cholesky | 11% | 8%
fft | 6% | 0%
lucon | 15% | 15%
lunon | 26% | 17%
ocean-con | 0% | 0%
ocean-non | 2% | 2%
radiosity | 22% | 10%
radix | 1% | 0%
raytrace | 22% | 0%
water-nsquared | 0% | 0%
water-spatial | 0% | 0%
Avg | 10% | 5%
Still require further tuning

## Slide 26
CPACT- Final Parameter Adjustment
Initial Impact Ordered Tuning
Size Adjustment
Final Parameter Adjustment
Evaluate one more configuration - double the line size
Energy decrease?
Stop tuning
Continue adjusting line size then associativity
no
yes
benchmark | final configuration | 
 | % diff | # cfgs exp
cholesky | 0% | 12
fft | 0% | 12
lucon | 0% | 9
lunon | 0% | 13
ocean-con | 0% | 8
ocean-non | 0% | 13
radiosity | 1% | 12
radix | 0% | 11
raytrace | 0% | 13
water-nsquared | 0% | 9
water-spatial | 0% | 9
Avg | 0% | 11
out of 1,296 configurations
1% of the design space

## Slide 27
CPACT- Final Parameter Adjustment
Initial Impact Ordered Tuning
Size Adjustment
Final Parameter Adjustment
Evaluate one more configuration - double the line size
Energy decrease?
Stop tuning
Continue adjusting line size then associativity
no
yes
benchmark | final configuration | 
 | % diff | # cfgs exp
cholesky | 0% | 12
fft | 0% | 12
lucon | 0% | 9
lunon | 0% | 13
ocean-con | 0% | 8
ocean-non | 0% | 13
radiosity | 1% | 12
radix | 0% | 11
raytrace | 0% | 13
water-nsquared | 0% | 9
water-spatial | 0% | 9
Avg | 0% | 11
out of 1,296 configurations
Execute the remainder of the application in the final configuration
1% of the design space

## Slide 28: Energy Savings - CPACT
CPACT achieved 24% average energy savings
  Dual-core optimal: 25% average energy savings
  1% average tuning energy overhead
    Execute in non-optimal, higher energy configurations
    Increase CPU stall energy during tuning
    Increase in static energy
Chart: Energy Savings (%)
| cholesky | fft | lucon | lunon | ocean-con | ocean-non | radiosity | radix | raytrace | water-nsquared | water-spatial | Avg
dual core (optimal) | 0.095185 | 0.18022 | 0.37447 | 0.2115 | 0.14394 | 0.014434 | 0.50195 | 0.32 | 0.26698 | 0.19081 | 0.44321 | 0.25498
CPACT | 0.096083 | 0.17382 | 0.37154 | 0.19345 | 0.1442 | 0.019794 | 0.49244 | 0.29771 | 0.26198 | 0.18897 | 0.43781 | 0.24344
24%
50%

## Slide 29: Performance - CPACT
Evaluated the performance in number of cycles
  Optimal: 5% average increase in cycles
  CPACT: 8% average increase in cycles
    3% tuning performance overhead – application execution stalled during tuning
  Even with the small performance overhead
    CPACT required an average of 62% of the number of cycles needed to complete execution on a single-core base system
    Or 1.6x speedup executing on a dual-core vs. single-core system
Chart: Normalized Performance
| cholesky | fft | lucon | lunon | ocean-con | ocean-non | radiosity | radix | raytrace | water-nsquared | water-spatial | Avg
dual core (optimal) | 1.0601 | 1.0696 | 1.0482 | 1.0585 | 1.041 | 0.98761 | 0.9514 | 1.1229 | 1.1233 | 1.1091 | 1.145 | 1.0554
CPACT | 1.0601 | 1.0696 | 1.0482 | 1.0585 | 1.041 | 1.1056 | 1.0137 | 1.123 | 1.1233 | 1.1091 | 1.145 | 1.0816
CPACT % of cycles | 0.6222 | 0.94186 | 0.55063 | 0.6752 | 0.52172 | 0.48762 | 0.61098 | 0.57354 | 0.72806 | 0.58969 | 0.55734 | 0.62353

## Slide 30: Application Analysis
Shared data introduces coherence misses
  Accounted for as much as 29% of the cache misses
  Coherence misses  as the cache size 
Applications with significant coherence misses
  Did not necessarily need a small cache
   cache size resulted in  coherence misses, but offset by  in total cache misses
Tuning coordination is more critical for applications with significant data sharing
  Coordinate size adjustment and final parameter adjustment steps
Data Sharing and Cache Tuning

## Slide 31: Application Classification
Do all cores need to run cache tuning?
Can we predict cache configurations based on application behavior?
  E.g., Similar work across all cores
    Tune one core, broadcast configuration
  E.g., One coordinating core (one configuration) and X working cores (all with same configuration)
    Only tune two cores, broadcast configuration for other X-1 working cores
Initial results
  Showed that similar number of accesses and misses aided in classification
  Details left for future work
P0
P1
P2
P3
P4
P5
P6
P7
P0
P1
P2
P3
P4
P5
P6
P7

## Slide 32: Conclusions
We developed the Conditional Parameter Adjustment Cache Tuner (CPACT) – a multi-core cache tuning heuristic
  Found optimal lowest energy cache configuration for 10 out of 11 SPLASH-2 applications
    Within 1% of optimal for remaining benchmark
  Average energy savings of 24%
  Searched only 1% of the 1,296 configuration design space
  Average performance overhead of 8% (3% due to tuning overheads)
Analyzed the effect of data sharing and workload decomposition on cache tuning
  Analysis can predict the tuning methodology for larger systems

## Slide 33: Questions?