## Slide 1
Exploiting Dynamic Phase Distance Mapping for Phase-based Tuning of Embedded Systems
+ Also Affiliated with NSF Center for High-Performance Reconfigurable Computing
This work was supported by National Science Foundation (NSF) grant CNS-0953447
Tosiron Adegbija and Ann Gordon-Ross+
Department of Electrical and Computer Engineering
University of Florida, Gainesville, Florida, USA

## Slide 2: Introduction and Motivation
Embedded systems are pervasive and have stringent design constraints
  Constraints: Energy, size, real time, cost, etc
System optimization is challenging due to numerous tunable parameters
  Tunable parameters: parameters that can be changed
    E.g., cache size, associativity, line size, clock frequency, etc
  Many combinations  large design space
  Phase-based tuning increases optimization potential
    How to determine a phase’s best configuration without significant runtime overhead?

## Slide 3
Base phase
Phase Pi
Cache characteristics | Cache configuration
Pb | Cb
Cache characteristics | Cache configuration
Pi | 
New phase
d (Pb, Pi)
Phase distance
Configuration distance
?
Previous Work: Phase Distance Mapping (PDM)
Previously characterized phase
Distance windows
Statically defined
phase distance
ranges
Configuration
change from
base phase’s
configuration

## Slide 4
PDM’s limitations
Phase Distance Mapping (PDM)
Distance windows
Statically defined
Design time overhead!!!
Needed to know/analyze
applications a priori
Unknown applications/
general purpose systems?
Base phase
Most prominent application
domain

## Slide 5
Contributions
Distance windows
Adapts to runtime application changes
Design time overhead!!!
Suitable for unknown applications/
general purpose systems
Base phase
Most prominent application
domain
Dynamically defined at runtime
Low overhead dynamic
method for determining a
phase’s best configuration!
Dynamically determined
No need to know/analyze
applications a priori
DynaPDM: Dynamic Phase Distance Mapping

## Slide 6: Results
  EDP savings calculated with respect to the base configuration
  DynaPDM achieved 28% average EDP savings overall
  Savings as high as 47% for 64M-rotatew2
  On average, within 1% of the optimal
  EDP improved over PDM by 8%
Chart: EDP normalized to the base cache configuration
| rotate-16x4Ms32w8 | rotate-16x4Ms4w8 | 64M-rotatew2 | rotate-4Ms4w1 | rotate-520k-270deg | rotate-color-4M-90degw1 | 4M-check | 4M-reassembly | 4M-tcp-mixed | ippktcheck-8x4M-4Worker | ipres-6M4worker | md5-128M4worker | md5-32M4worker | md5-4M | empty-wld | huffde-all | Average
Optimal | 0.74414 | 0.64174 | 0.52653 | 0.73571 | 0.60809 | 0.73108 | 0.79808 | 0.75467 | 0.7586 | 0.79374 | 0.73587 | 0.71347 | 0.71958 | 0.67005 | 0.72858 | 0.73302 | 0.71206
PDM | 0.74414 | 0.64174 | 0.52653 | 0.73571 | 0.60886 | 0.79824 | 0.81531 | 0.75467 | 0.84399 | 0.8432 | 0.73587 | 0.72184 | 0.79286 | 0.72527 | 0.77465 | 0.80924 | 0.74201
DynaPDM | 0.74414 | 0.64956 | 0.52653 | 0.75051 | 0.60886 | 0.73108 | 0.79808 | 0.75467 | 0.76151 | 0.79374 | 0.73587 | 0.72184 | 0.71958 | 0.68794 | 0.72858 | 0.75267 | 0.71657
28%
DynaPDM improved over PDM and eliminated design-time effort!
47%
DynaPDM’s
configurations
1% of
the optimal!