## Slide 1: Enabling Right-Provisioned Microprocessor Architectures for the Internet of Things Tosiron Adegbija1, Anita Rogacs2, Chandrakant Patel2, and Ann Gordon-Ross3+ 1Department of Electrical and Computer Engineering University of Arizona, Arizona, USA 2Hewlett-Packard (HP) Laboratories Palo Alto, California, USA 3Department of Electrical and Computer Engineering University of Florida, Florida, USA +Also Affiliated with NSF Center for High-Performance Reconfigurable Computing
This work was supported in part by National Science Foundation (NSF) grant CNS-0953447

## Slide 2: Introduction
Internet of Things (IoT): pervasive presence of uniquely identifiable, connected devices
Goal: Reduce reliance on human intervention for data acquisition, visualization and use

## Slide 3: Motivation – IoT Impact
Wide-ranging use-cases
  Healthcare, manufacturing, smart cities, transportation
  Transformative to work, life, and the global economy
26 billion devices by 2020
$3 trillion economic impact
[Gartner Research, 2014]

## Slide 4: Traditional IoT Model and Challenges
Transmission is expensive
Bandwidth bottleneck
Real-time constraints
Complex applications
Increased energy consumption and latency
Head node
Edge node
Edge node
Edge node
Edge node
Edge node

## Slide 5: IoT Optimization
Edge Computing
  Move computations to the edge nodes
Example
  Medical diagnostics
Requirements
  Sufficient compute power
  Maintain low-energy
  Maintain form factor
What microprocessor architectures will support edge computing?

## Slide 6: Contributions
Propose broad and tractable classification of IoT applications
  Identify key application functions
Evaluated state of the art microprocessor characteristics
  Focus on CPU component
Identify highest impact microarchitecture characteristics
  Enable efficient design space exploration
  Impact of leakage power optimization
Lay foundation for right-provisioning of IoT device microprocessors

## Slide 7: Determining a Right-Provisioned Architecture
Image capture | Sensing | Memory intensity
 | Image processing | Compute/memory intensity, parallelism
Face detection | Image processing | Compute/memory intensity, parallelism
Face recognition | Image processing | Compute/memory intensity, parallelism
Data encryption | Security | Compute intensity
Data transmission | Compression | Compute intensity
 | Communication | Compute intensity
IoT
use case
Execution characteristics
Applications
Application functions
Right-provisioned architecture

## Slide 8: IoT Application Classification
Surveyed several IoT use-cases
Classified applications based on functions
Application function | Benchmark | Benchmark description
Sensing | matrixTrans (_128, _256, _512, _1024) | Dense matrix transpose of n × n matrix
Communications | fft (_small and _large) | Fast Fourier Transform
Image processing | matrixMult (_128, _256, _512) | Dense matrix multiplication of n × n matrix
Lossy compression | jpeg (_small and _large) | Joint Photographic Experts Group (JPEG) compression
Lossless compression | lz4 (_mr and _xray) | Lossless data compression
Security | sha (_small and _large) | Secure hash algorithm
Fault tolerance | crc (_small and _large) | Cyclic redundancy check

## Slide 9: IoT Microarchitecture Configurations
Surveyed state of the art IoT microprocessors
  Ranging from microcontrollers to high-performance embedded systems microprocessors
  Goal: Identify technology gaps in state of the art
 | Conf1 | Conf2 | Conf3 | Conf4
Sample CPU | ARM Cortex M4 | Intel Quark | ARM Cortex A7 | ARM Cortex A15
Frequency | 48 MHz | 400 MHz | 1 GHz | 1.9 GHz
Number of cores | 1 | 1 | 4 | 4
Pipeline stages | 3 | 5 | 8 | 15
Cache | None | None | 32 KB i/d L1, 1MB L2 | 32 KB i/d L1, 2MB L2
Memory | 512 KB flash | 2 GB RAM | 2 GB support | 1 TB RAM support
Execution | In-order | In-order | In-order | Out-of-order

## Slide 10: Experimental Methodology
Simulators
  GEM5 Simulator
  Did not simulate the impact of parallelism
  McPAT: power
  Perl scripts to drive simulations
Analysis
  Execution characteristics: memory and compute intensity
  Impact of different data sizes
  Benchmarks’ execution time, energy, performance and efficiency
  Sensitivity to clock frequency, inorder vs. out-of-order execution, cache sizes
  Impact of idle energy/power optimization

## Slide 11: Execution characteristics
Memory references per instruction (MPI) and Instructions per Cycle (IPC)
Similar characteristics for different data sizes
  Exception: matrixTrans and matrixMult
MatrixTrans: IPC reduction from 128 to 512
MatrixMult: IPC reduction from 256 to 512
Notes: Evaluated on conf4
MPI is microarchitecture-independent; IPC is microarchitecture-dependent
MatrixTrans is the most memory intensive (memory intensity has to do with memory references per instruction, and not data sizes)
FFT is compute intensive but not memory intensive (relative to the other benchmarks)
SHA is both memory intensive and compute intensive

## Slide 12: Comparison of the Configurations
Chart: Execution time normalized to conf4
| cjpeg_small | cjpeg_large | lz4_mr | lz4_xray | matrixTrans_128 | matrixTrans_256 | matrixTrans_512 | matrixTrans_1024 | crc_small | crc_large | sha_small | sha_large | fft_small | fft_large | matrixMult_128 | matrixMult_256 | matrixMult_512 | AVERAGE
conf1 | 172.972 | 0 | 0 | 0 | 173.2865 | 0 | 0 | 0 | 112.4406 | 112.4921 | 351.5333 | 359.4121 | 156.6211 | 0 | 177.5175 | 0 | 0 | 202.0344
conf2 | 20.94 | 20.9334 | 29.3437 | 31.483 | 23.4468 | 15.9517 | 6.4046 | 6.4637 | 13.4933 | 13.4991 | 42.2052 | 43.1315 | 18.9608 | 17.7293 | 22.3034 | 21.7087 | 10.3801 | 21.0811
conf3 | 8.4196 | 8.5433 | 11.7762 | 12.4476 | 10.7446 | 9.302 | 3.7272 | 3.7679 | 5.398 | 5.3997 | 16.9091 | 17.2553 | 7.5321 | 7.0613 | 9.1685 | 10.2566 | 4.9016 | 8.9771
Energy and execution time normalized to conf4 for a single execution
Chart: Energy normalized to conf4
| cjpeg_small | cjpeg_large | lz4_mr | lz4_xray | matrixTrans_128 | matrixTrans_256 | matrixTrans_512 | matrixTrans_1024 | crc_small | crc_large | sha_small | sha_large | fft_small | fft_large | matrixMult_128 | matrixMult_256 | matrixMult_512 | AVERAGE
conf1 | 32.6838 | 33.7421 | 24.7231 | 24.7227 | 50.0439 | 50.5518 | 28.9988 | 32.9929 | 34.8074
conf2 | 4.7036 | 4.7544 | 6.0174 | 6.349 | 5.399 | 4.1723 | 1.9643 | 1.9788 | 3.5283 | 3.5293 | 7.1399 | 7.2092 | 4.1864 | 3.9903 | 4.9317 | 4.8615 | 2.9915 | 4.571
conf3 | 4.5316 | 4.6426 | 5.7682 | 5.9966 | 5.8349 | 5.6574 | 2.6585 | 2.6822 | 3.3843 | 3.385 | 6.8553 | 6.9128 | 4.0064 | 3.8299 | 4.854 | 5.4384 | 3.3449 | 4.6931
Conf1 could not execute some applications due to insufficient memory
Conf4 outperforms all configurations for a single execution
  Energy does not take into account idle energy
  For specific latency requirements, only benchmark on one configuration and extrapolate to others
Notes: Mention that this does not include the effect of leakage power.
Execution time: Conf1, conf2, and conf3 increase 202x, 23x, and 9x.
Run on conf4, estimate performance on smaller configurations
Energy: conf1, conf2, and conf3 increase 35x, 4.6x, and 4.7x

## Slide 13: Comparison of the Configurations
Chart: Performance (GOPS) normalized to conf4
| cjpeg_small | cjpeg_large | lz4_mr | lz4_xray | matrixTrans_128 | matrixTrans_256 | matrixTrans_512 | matrixTrans_1024 | crc_small | crc_large | sha_small | sha_large | fft_small | fft_large | matrixMult_128 | matrixMult_256 | matrixMult_512 | average
conf1 | 0.0057437 | 0 | 0 | 0 | 0.0057693 | 0 | 0 | 0 | 0.0088934 | 0.0088894 | 0.0028221 | 0.0027603 | 0.0062761 | 0 | 0.005521 | 0 | 0.0058344
conf2 | 0.047445 | 0.047677 | 0.033805 | 0.031458 | 0.042639 | 0.062698 | 0.15615 | 0.15479 | 0.07411 | 0.074078 | 0.023506 | 0.023002 | 0.051842 | 0.055376 | 0.043943 | 0.045145 | 0.060479
conf3 | 0.11798 | 0.11682 | 0.084235 | 0.079139 | 0.093046 | 0.10752 | 0.26832 | 0.26554 | 0.18525 | 0.18519 | 0.05867 | 0.057495 | 0.1305 | 0.13903 | 0.10689 | 0.095552 | 0.1307
Performance (GOPS) and efficiency (GOPS/W) normalized to conf4
Conf1, conf2, and conf3 had 33x, 4x, and 4x worse efficiency than conf4, respectively
Conf1, conf2, and conf3 had 171x, 17x, and 8x worse performance than conf4, respectively
What are the highest-impact microarchitectural characteristics?
Chart: Efficiency normalized to conf4
| cjpeg_small | cjpeg_large | lz4_mr | lz4_xray | matrixTrans_128 | matrixTrans_256 | matrixTrans_512 | matrixTrans_1024 | crc_small | crc_large | sha_small | sha_large | fft_small | fft_large | matrixMult_128 | matrixMult_256 | matrixMult_512 | average
conf1 | 0.030397 | 0.029639 | 0.040447 | 0.040435 | 0.019824 | 0.019625 | 0.033897 | 0.029705 | 0.030496
conf2 | 0.21122 | 0.20992 | 0.16485 | 0.15599 | 0.18517 | 0.23971 | 0.50911 | 0.50562 | 0.28342 | 0.28334 | 0.13894 | 0.13762 | 0.2348 | 0.24604 | 0.19873 | 0.20159 | 0.21699 | 0.24253
conf3 | 0.21921 | 0.21498 | 0.17197 | 0.16428 | 0.17134 | 0.17678 | 0.37618 | 0.37302 | 0.29547 | 0.29542 | 0.14471 | 0.14352 | 0.24535 | 0.25634 | 0.20191 | 0.18021 | 0.29296 | 0.2308
Notes: Similar results to previous slides.

## Slide 14: Impact of Clock Frequency
1 GHz clock frequency normalized to 1.9 GHz (evaluated on conf4)
1 GHz increased execution time and energy by 62% and 32% on average
  No execution time change for matrixTrans
1 GHz reduced energy by 4% for matrixTrans
1 GHz reduced performance and efficiency by 40% and 27% on average
  4% efficiency improvement for matrixTrans
Chart: Execution time and energy normalized to conf4
| cjpeg_large | lz4_mr | matrixTrans_1024 | crc_large | sha_large | fft_large | matrixMult_128 | AVERAGE
Time | 1.8558 | 1.8014 | 1.0043 | 1.9 | 1.8987 | 1.8993 | 1.8976 | 1.6225
Energy | 1.4988 | 1.4219 | 0.96497 | 1.6029 | 1.3852 | 1.5168 | 1.5082 | 1.3204
Chart: Performance and efficiency normalized to conf4
| cjpeg_large | lz4_mr | matrixTrans_1024 | crc_large | sha_large | fft_large | matrixMult_128 | AVERAGE
GOPS | 0.53958 | 0.55512 | 0.99627 | 0.52632 | 0.52666 | 0.52652 | 0.52697 | 0.59963
GOPS/W | 0.6681 | 0.7033 | 1.0368 | 0.62386 | 0.72187 | 0.65932 | 0.66306 | 0.72519
Notes: To see which microarchitectural characteristics have the highest impact
Mention that conf4 is the baseline

## Slide 15: Impact of Execution Order
Chart: Time and energy normalized to conf4
| cjpeg_large | lz4_mr | matrixTrans_1024 | crc_large | sha_large | fft_large | matrixMult_128 | AVERAGE
Time | 4.501 | 6.2556 | 2.3154 | 2.8419 | 9.0825 | 3.7158 | 4.8255 | 4.7911
Energy | 2.8592 | 3.5688 | 1.8625 | 2.0865 | 4.2579 | 2.373 | 2.9907 | 2.8569
Inorder normalized to out-of-order (evaluated on conf4)
Chart: Performance and efficiency normalized to conf4
| cjpeg_large | lz4_mr | matrixTrans_1024 | crc_large | sha_large | fft_large | matrixMult_128 | AVERAGE
GOP | 0.22173 | 0.15857 | 0.43211 | 0.35187 | 0.10923 | 0.26422 | 0.2031 | 0.24869
GOP/W | 0.34905 | 0.27796 | 0.53718 | 0.47927 | 0.233 | 0.41372 | 0.3277 | 0.37398
Inorder average 4.8x slower than OoO
  As high as 9x for sha
Inorder consumes average 2.9x more energy than OoO
Inorder 4.8x and 2.9x worse performance and efficiency, respectively
Notes: Big picture: OoO is the better option, complexity depends on specific implementation
Execution order has the biggest impact on overall performance and energy consumption.
Bigger impact for more compute intensive and memory intensive benchmarks: can continue computations while waiting for memory

## Slide 16: Impact of Cache Sizes
Chart: Time and energy normalized to conf4
| cjpeg_large | lz4_mr | matrixTrans_1024 | crc_large | sha_large | fft_large | matrixMult_128 | AVERAGE
Time | 1.0477 | 1.1777 | 0.99905 | 1 | 0.99978 | 1.0309 | 1.0029 | 1.0369
Energy | 0.96286 | 1.0307 | 0.92189 | 0.93248 | 0.94734 | 0.95669 | 0.94279 | 0.95639
Chart: Performance and efficiency normalized to conf4
| cjpeg_large | lz4_mr | matrixTrans_1024 | crc_large | sha_large | fft_large | matrixMult_128 | AVERAGE
GOP | 0.95621 | 0.84907 | 1.001 | 1 | 1.0002 | 0.96957 | 0.99706 | 0.96758
GOP/W | 1.0405 | 0.9702 | 1.0848 | 1.0724 | 1.0556 | 1.0448 | 1.0607 | 1.047
16 K data cache normalized to 32 K cache (evaluated on conf4)
Very little change in execution time (< 4%)
16K consumes about 4% less energy
16K degrades performance by 3% on average
16K improves efficiency by 5% on average

## Slide 17: Impact of Cache Sizes
Data cache miss rates: 16 K cache normalized to 32 K
16K results in average 18% more cache miss rates than 32K
  As high as 82% for lz4
No change for matrixTrans, crc, and matrixMult
Chart: Data cache miss rates normalized to 32k
| cjpeg_large | lz4_mr | matrixTrans_1024 | crc_large | sha_large | fft_large | matrixMult_128 | AVERAGE
Norm to 32k | 1.3495 | 1.8224 | 1.0054 | 1 | 1 | 1.0978 | 1.0001 | 1.1822

## Slide 18: Impact of Idle Energy on Overall Energy Consumption
Sensor readings every 40s
Energy consumed in 1 hour
  90 readings
CRC every 10 mins
Energy consumed in 1 hour
  6 computations
Chart: crc_large - longest
| conf1 | conf2 | conf3
energy | 0.32348 | 0.3476 | 0.7686
Chart: matrixTrans – shortest
| conf1 | conf2 | conf3
energy | 0.27048 | 0.34145 | 0.76322
27%
34%
76%
32%
35%
76%
Conf1 consumes least energy overall
Conf3 and conf4 have high leakage power
Can the idle energy be optimized?
Execution of a single benchmark
Notes: Complete opposite of single executions
Without optimization, conf1 is the best option
What happens when we optimize the energy across all the configurations?

## Slide 19: Impact of Idle Energy on Overall Energy Consumption
Sensor readings every 40s
Energy consumed in 1 hour
  90 readings
Conf1 provides the most benefit
CRC every 10 mins
Energy consumed in 1 hour
  6 computations
Conf2 provides the most benefit
Impact of power gating depends on
application run time
Chart: crc_large - longest
| conf1 | conf2 | conf3
withPowerGating | 2.4036 | 0.61875 | 0.99158
Chart: matrixTrans - shortest
| conf1 | conf2 | conf3
withPowerGating | 0.28359 | 0.34343 | 0.76521
Impact of power gating: 95% leakage power reduction

## Slide 20: Impact of Idle Energy on Overall Energy Consumption
Execution of multiple benchmarks
Six applications in succession every 10 mins
Energy consumed in 1 hour
  6 computations
Conf2 provides the most benefit without power gating
Conf4 provides the most benefit with power gating
Chart: Total energy normalized to conf4
| conf2 | conf3
noPowerGating | 0.43598 | 0.844
withPowerGating | 1.7978 | 2.0047
Longer executions on larger configurations provide greater optimization benefit
Notes: Conf1 could not run these benchmarks (selected randomly)

## Slide 21: Conclusions
Explored architectural support for the Internet of Things (IoT)
  Foundation for further research
  Proposed IoT application functions and benchmarks
  Quantified impact of execution order, frequency, and cache sizes
  Showed that power optimization depends on configuration and application runtime
Enabling right-provisioning for IoT devices
  Our work helps to reduce design space exploration
  Given application requirements, estimate configurations
Notes: Given application requirements, our work provides a framework for analyzing IoT devices and selecting the best configurations for edge computing on the IoT.

## Slide 22: Questions and Comments