## Slide 1
Parallelized Benchmark-Driven Performance Evaluation of SMPs and Tiled Multi-Core Architectures for Embedded Systems
Arslan Munir*, Ann Gordon-Ross+ , and Sanjay Ranka#
Department of Electrical and Computer Engineering
#Department of Computer and Information Science and Engineering
*Rice University, Houston, Texas
+#University of Florida, Gainesville, Florida, USA
This work was supported by the Natural Sciences and Engineering Research Council of Canada (NSERC) and the National Science Foundation (NSF) (CNS-0953447 and CNS-0905308)
+ Also affiliated with NSF Center for High-Performance Reconfigurable Computing

## Slide 2: Introduction and Motivation
Systems within or
embedded into
other systems
Automotive
Medical
Applications
Embedded
Systems
Space
Consumer
Electronics

## Slide 3: Introduction and Motivation
Multi-core embedded systems
  Moore’s law supplying billion of transistors on-chip
  Increased computing demands from embedded system with constrained energy/power
    A 3G mobile handset’s signal processing requires 35-40 GOPS
      Constraints: power dissipation budget of 1W
      Performance efficiency required: 25 mW/GOP or 25 pJ/operation
  Multi-core embedded systems provide a promising solution
  to meet these performance and power constraints
Multi-core embedded systems architecture
  Processor cores
  Caches: level one instruction (L1-I), level one data (L1-D),
  last-level caches (LLCs) level two (L2) or level three (L3)
  Memory controllers
  Interconnection network
Challenge: Evaluation of
diverse multi-core architectures
Many architectures support
different parallel programming
languages
Motivation: Proliferation of diverse
multi-core architectures

## Slide 4: Introduction and Motivation
Benchmark-driven
simulative approach
Multi-core Architecture
Evaluation Approaches
Benchmark-driven
experimental approach
Analytical modeling
approach
+ Good method for design evaluation
‒ Requires an accurate multi-core simulator
‒ Requires representative and diverse benchmarks
‒ Lengthy simulation time
+ Most accurate
+ Faster than simulative
‒ Cannot be used for design tradeoff evaluation
‒ Requires representative and diverse benchmarks
+ Fastest
+ Benchmarks are not required
‒ Accurate model development is challenging
‒ Trades off accuracy for faster evaluation
Focus of our work
Benchmark runs on a multi-core simulator
Benchmark runs on
a physical multi-core
platform
Models the multi- core architectures

## Slide 5: Contributions
Evaluates symmetric multiprocessors (SMPs)
and tiled multi-core architectures (TMAs)
Parallelized benchmarks
  Information fusion application
  Gaussian elimination (GE)
  Embarrassingly parallel (EP)
Benchmarks parallelization
for SMPs using OpenMP
Benchmarks parallelization
for TMAs (TILEPro64)
using Tilera’s ilib API
First work to
cross-evaluate
SMPs and TMAs
Performance metrics
  Execution time
  Speedup
  Efficiency
  Cost
  Performance
  Performance per watt

## Slide 6: Related Work
Parallelization and performance analysis
  Sun et al. [IEEE TPDS, 1995] investigated performance metrics (e.g., speedup, efficiency, scalability) for shared memory systems
  Brown et al. [Springer LNCS, 2008] studied performance and programmability comparison for Born calculation using OpenMP and MPI
  Zhu et al. [IWOMP, 2005] studied performance of OpenMP on IBM Cyclops-64 architecture
  Our work differs from the previous parallelization and performance analysis work
    Compares performance of different benchmarks using OpenMP and Tilera’s ilib API
    Compares two different multi-core architectures
Multi-core architectures for parallel and distributed embedded systems
  Dogan et al. [PATMOS, 2011] evaluated single- and multi-core architectures for biomedical signal processing in wireless body sensor networks (WBSNs)
  Kwok et al. [ICPPW, 2006] proposed FPGA-based multi-core computing for batch processing of image data in distributed embedded wireless sensor networks (EWSNs)
  Our work differs from the previous work
    Parallelize information fusion application and GE for two multi-core architectures

## Slide 7: Symmetric Multiprocessors (SMPs)
SMPs  most pervasive and prevalent type of multi-core architecture
SMP architecture
  Symmetric access to all of main memory
  from any processor core
  Each processor has a private cache
  Processors and memory modules attach
  to a shared interconnect  typically a shared bus
SMP  in this work
  Intel-based SMP
  8-core SMP
    2x Intel’s Xeon E5430 quad-core processor (SMP2xQuadXeon)
    45 nm CMOS lithography
    Maximum clock frequency  2.66 GHz
    32 KB L1-I and 32 KB L1-D cache per Xeon E5430 chip
    12 MB unified L2 cache per Xeon E5430 chip

## Slide 8: Tiled Multi-core Architectures (TMAs)
Tilera’s TILEPro64
Many-core Chip
A processor core with a switch
Tile
Interconnection Network
Connects tiles on the chip
TMA Examples
Raw processor
Intel’s Tera-Scale
research processor
Tilera’s TILE64
Tilera’s TILEPro64
TILEPro64
8x8 grid of 64 tiles
Each tile
  3-way VLIW pipe-lined
  max clock frequency
    866 MHz
Private L1 and L2 cache
Dynamic Distributed Cache (DDC)

## Slide 9: Benchmarks
Information Fusion
  A crucial processing task in distributed embedded systems
  Condenses the sensed data from different sources
  Transmits selected fused information to a base station node
    Important  applications with limited transmission bandwidth (e.g., EWSNs)
  Considered Application
    Cluster  10 sensor nodes
      Attached sensors: Temperature, pressure, humidity, acoustic, magnetometer,
            accelerometer, gyroscope, proximity, orientation
    Cluster head
      Implements moving average filter  reduces noise from measurements
      Calculates minimum, maximum, and average of sensed data
      O(NM) operations
        N  number of samples to be fused
        M  moving average window size

## Slide 10: Benchmarks
Gaussian Elimination
  Solves a system of linear equations
  Used in many scientific applications
    LINPACK benchmark  ranks supercomputers
    Decoding algorithm for network coding  Variant of GE
  O(n3) operations
    n  number of linear equations to be solved
Embarrassingly Parallel
  Quantifies the peak attainable performance of a parallel architecture
  Generation of normally distributed random variates
    Box-Muller’s algorithm
    99n floating point (FP) operations
      n  number of random variates to be generated

## Slide 11: Parallel Computing Device Metrics
Parallel Computing
Device Metrics
Run Time
Serial run time Ts
  Time elapsed between
  the beginning and the
  end of the program
Parallel run time Tp
  Time elapsed from the
  the beginning of a
  program to the moment
  last processor finishes
  execution
Measures the fraction
of time for which the
processor is usefully
employed
E = S/p
Measures the system capacity
to increase speedup in proportion
to the number of processors
Helps in comparing
different architectures
Speedup
Efficiency
Cost
Scalability
Measures the performance
gain achieved by parallelization
S = Ts/Tp
Measures the sum
of time that each
processor spends
solving the problem
C = Tp . p

## Slide 12: Results – Information Fusion Application
Performance results for the information fusion application for SMP2xQuadXeon when M = 40
The multi-core processor speeds up the execution time as compared to a single-core processor
The multi-core processor  the throughput (MOPS) as compared to a single-core processor
The multi-core processor  the power-efficiency as compared to a single-core processor
  Four processor cores (p = 4) attain 49% better performance per watt than a single-core
N denotes the number
of samples to be fused
M is moving average filter’s window size
Results are obtained with compiler optimization level -O3

## Slide 13: Results – Information Fusion Application
Performance results for the information fusion application for TILEPro64 when M = 40
The multi-core processor speeds up the execution time
  Speedup is proportional to the number of tiles p (i.e., ideal speedup)
The efficiency remains close to 1 and cost remains constant indicating ideal scalability
The multi-core processor  the throughput and power-efficiency as compared to a single-core processor
  Increases MOPS by 48.4x and MOPS/W by 11.3x for p = 50
Results are obtained with compiler optimization level -O3

## Slide 14: Results – Information Fusion Application
Performance per watt (MOPS/W) comparison between SMP2xQuadXeon and TILEPro64 for the information fusion application when N = 3000,000
Operation on private data of various sensors/sources  very well parallelizable using Tilera’s ilib API
TILEPro64 exploits data locality
OpenMP sections and parallel construct requires sensed data to be shared by operating threads
TILEPro64 delivers higher performance per watt as compared to SMP2xQuadXeon
TILEPro64 attains 466% better performance per watt than the SMP for
p = 8

## Slide 15: Results – Gaussian Elimination
Performance results for the Gaussian elimination benchmark for SMP2xQuadXeon
The multi-core processor speeds up the execution time as compared to a single-core processor
  Speedup is proportional to the number of tiles p (i.e., ideal speedup)
The efficiency remains close to 1 and cost remains constant indicating ideal scalability
The multi-core processor  the throughput and power-efficiency as compared to a single-core processor
  Increases MOPS by 7.4x and MOPS/W by 2.2x for p = 8
m is the number of linear equations and
n is the number of variables in a linear equation
Results are obtained with compiler optimization level -O3

## Slide 16: Results – Gaussian Elimination
Performance results for the Gaussian elimination benchmark for TILEPro64
The multi-core processor speeds up the execution time
  Speedup is much less than the number of tiles p
The efficiency  and cost  as p  indicating poor scalability
The multi-core processor  the throughput and power-efficiency as compared to a single-core processor
  Increases MOPS by 14x and MOPS/W by 3x for p = 56
Results are obtained with compiler optimization level -O3

## Slide 17: Results – Gaussian Elimination
Performance per watt (MFLOPS/W) comparison between SMP2xQuadXeon and TILEPro64 for the GE benchmark when (m, n) = (2000, 2000)
Lots of communication and synchronization operations  favors SMPs as communication transforms to read & write in shared memory
Higher external memory bandwidth of the SMP helps attaining better performance than TILEPro64
SMP2xQuadXeon delivers higher MFLOPS/W than TILEPro64
SMP2xQuadXeon attains 563% better performance per watt than TILEPro64 for p = 8

## Slide 18: Insights Obtained from Parallelized Benchmark-Driven Evaluation
Compiler optimization flag – O3  optimizes performance both for SMPs and TMAs
The multi-core processor  speeds up, throughput, and power-efficiency as compared to a single-core processor both for SMPs and TMAs
State-of-the-art SMPs outperform TMAs in terms of execution time
  For EP benchmark: Intel-based SMP  4x better performance per watt when p = 8
TMAs can provide comparable performance per watt as that of SMPs
TMAs outperforms SMPs for applications
  More private data
  Little dependency
  Data locality
For information fusion application: TILEPro64 efficiency  close to 1 and
cost  constant  ideal scalability
  TILEPro64  466% better performance per watt than an Intel-based SMP when p = 8
SMPs outperforms TMAs for applications
  Excessive synchronization
  Excessive dependency
  Shared data
For GE benchmark: Intel-based SMP  563% better perf./watt than TILEPro64 when p = 8

## Slide 19: Questions?