## Slide 1
Analysis of Cache Tuner Architectural Layouts for Multicore Embedded Systems
+ Also Affiliated with NSF Center for High-Performance Reconfigurable Computing
This work was supported by National Science Foundation (NSF) grant CNS-0953447
Tosiron Adegbija1, Ann Gordon-Ross1+,and Marisha Rawlins2
1Department of Electrical and Computer Engineering
University of Florida, Gainesville, Florida, USA 2Center for Information and Communication Technology University of Trinidad and Tobago, Trinidad and Tobago

## Slide 2: Introduction and Motivation
Embedded systems are ubiquitous and have stringent design constraints
  Increasing demand for high performance embedded systems
Shift to multicore embedded systems
  Increases system and optimization complexity
Need optimizations that reduce power without increasing overheads
  Overheads: performance, area, etc.

## Slide 3: Optimization – Cache Tuning
Caches are a good candidate for optimization
  Significant impact on power and performance
Different applications have different cache parameter value requirements
  Parameter values: cache size, line size, associativity
Cache tuning determines appropriate/optimal parameter values (cache configurations) to meet optimization goals (e.g., lowest energy)
Tunable cache
Cache tuner
Download application
Microprocessor
Cache tuning requires
- tunable/configurable cache
- tuning hardware (cache tuner)
- tuning hardware (cache tuner)

## Slide 4: Configurable Cache Architecture
Configurable caches enable cache tuning
  Design space: combination of all possible configurations
A Highly Configurable Cache (Zhang ‘03)
2KB
2KB
2KB
2KB
8 KB, 4-way base cache
2KB
2KB
2KB
2KB
8 KB, 2-way
2KB
2KB
2KB
2KB
8 KB, direct-mapped
Way concatenation
Tunable Associativity
2KB
2KB
2KB
2KB
4 KB, 2-way
2KB
2KB
2KB
2KB
2 KB, direct-mapped
Way shutdown
Tunable Size
Configurable Line size
16 byte physical line size
Tunable Line Size

## Slide 5: Cache Tuners
Tuner evaluates different configurations to determine the best configuration
  Implements tuning algorithm/heuristic to search design space
  Best configuration satisfies design objective (e.g., minimum energy/execution time)
  Can impose overheads (tuning delay, power, area) and complexity
Software cache tuners
    Intrusive to application and cache
      Non-optimal, inferior configurations
Hardware cache tuners
    Non-intrusive to application
    Must be low-overhead
Previous work
  Single- and dual-core cache tuners
More cores = more tuner overhead/complexity
Number of cores
Tuner overhead and
complexity
Number of cores
Tuner overhead/complexity
Need low-overhead cache tuners for multicore systems!
Notes: Cache tuners can impose additional overheads
  Tuning delay: cycles elapsed during tuning – may stall the processor
Options for cache tuners
  Software: intrusive, affects application and cache behavior due to context switching
    Can select non-optimal configurations
  Hardware: non-intrusive, must be low overhead
Previous work: single and dual-core cache tuners
  Additional cores increase design complexity

## Slide 6: Cache Tuner Architectural Layouts
Global tuner
  Single tuner for all cores
  Shared resource bottleneck
    Tuning delay
  Little area/power
Core 1
L1 Cache
Core 2
L1 Cache
Core 3
L1 Cache
Core 4
L1 Cache
Tuner
Global tuner
Tuning delay
Area overhead
Power overhead
Overheads incurred

## Slide 7: Cache Tuner Architectural Layouts
Dedicated tuners
Core 1
L1 Cache
Core 2
L1 Cache
Core 3
L1 Cache
Core 4
L1 Cache
Tuner 2
Tuner 1
Tuner 3
Tuner 4
Tuning delay
Area overhead
Power overhead
Overheads incurred
Dedicated tuners
  Separate tuner for each core
  Resources not shared
    Less tuning delay
  More area/power

## Slide 8: Cache Tuner Architectural Layouts
Clustered tuners
Core 1
L1 Cache
Core 2
L1 Cache
Core 3
L1 Cache
Core 4
L1 Cache
Tuner 1
Tuner 2
Tuning delay
Area overhead
Power overhead
Overheads incurred
Clustered tuners
  Separate tuner for core subset
  Shared resources
    Tuning delay
  Tradeoff area/power and tuning delay
Cluster size must be carefully selected!

## Slide 9: Contributions
Challenges
  Low-overhead tuners required for > dual core systems
  Cluster sizes must be carefully selected
    Tradeoff power, area, and shared resource contention
Our work
  Design custom cache tuners for multicore embedded systems
    Scalable
    Low-overhead
  Quantify tradeoffs of cache tuner architectural layouts
  Formulate essential design guidelines for cache tuners

## Slide 10: Hardware Implementation
Cache tuner
Implemented cache tuners in multiple architectural layouts
  2-, 4-, 8-, and 16-core systems
State machine
Datapath
Core1
Core2
Core3
Core4
Global tuner
Core1
Core2
Core3
Core4
Dedicated tuners
Core1
Core2
Core3
Core4
Clustered tuners

## Slide 11: State Machine
calculates energy consumption
changes the value of the parameter being tuned
changes the parameter being tuned
C5
C4
C1
C2
C3
C0
tune_again =
1, next parameter value
0, next parameter
{
busy bit
C1 – Dynamic energy
C2 – Static energy
C3 – Write back energy
C4 – Cache fill energy
C5 – CPU stall energy
V0
V1
V2
V3
V4
V5
2
16
1-way
4
32
2-way
8
64
4-way
16
---
---
32
---
---
configuration bits
adjust_parameter
size (KB)
line_size (byte)
associativity
S0
S1
S3
S4
adjust_parameter
= none
adjust_parameter
= size
adjust_parameter
= line_size
adjust_parameter
= associativity
start = 1
start = 0
Value state
Parameter state
Calculation state
tune_again = 0
start = 1
calc_done = 1
calc_start = 1
tune_again = 1
Datapath
control signal
control
signals

## Slide 12: Datapath
State machine
for cores
C(0)… C(n-1)
control
signals
accesses_p(n)
total_cycles_p(n)
miss_cycles_p(n)
write_backs_p(n)
MUX
MUX
dynamic_energy
static_energy
fill_energy
write_back_energy
cpu_stall_energy
configuration bits
register
register
X
register
+
comparator
current_energy
previous_energy
Multiply accumulate (MAC) unit
Datapath

## Slide 13: Experimental Setup
Cache tuners evaluated
  Global and dedicated tuners: 2-, 4-, 8-, and 16-cores
  Clustered tuners:
    4-, 8-, and 16-cores: 2-core clusters
    8- and 16-cores: 4-core clusters
    16-cores: 8-core clusters
Modeled with synthesizable VHDL in Synopsys Design Compiler
11 benchmarks from Splash-2 benchmark suite
SESC simulator provided cache statistics

## Slide 14: Power and Area Trends
Power-of-two increase:
Global tuner = 49%
Dedicated tuners = 89%
Clustered tuners = 111%
Power-of-two increase:
Global tuner = 51%
Dedicated tuners = 93%
Clustered tuners = 100%
Power
Area
Linear increases: scalability of all layouts to future systems

## Slide 15: Tuning Delay
Small clusters reduce bottleneck in large systems
Average reduction normalized to global tuner:
Dedicated tuners = 3%, 20%, 21%, and 82% in 2-, 4-, 8-, 16-core systems, respectively
2/cluster tuners = 17%, 18%, 82% in 4-, 8-, 16-core systems, respectively
4/cluster tuners = 1% and 78% in 8- and 16-core systems, respectively
8/cluster tuners = 77% in 16-core system

## Slide 16: Power/Area Compared to Global Tuner
Power increase:
Dedicated tuners = 149%
2/cluster tuners = 86%
4/cluster tuners = 56%
8/cluster tuners = 53%
Clustered tuners can provide good tradeoff in large systems
Area increase:
Dedicated tuners = 156%
2/cluster tuners = 87%
4/cluster tuners = 44%
8/cluster tuners = 23%
Power
Area

## Slide 17: Overheads Imposed on Microprocessors
Compared to MIPS32 M14K 90nm processor: 12mW power at 200 MHz; 0.21mm2 area
Global = 0.5%
Dedicated tuners = 1.16%
Clustered tuners = 0.6%
Our cache tuners constitute minimal overhead!
Power
Area
Global = 4.73%
Dedicated tuners = 11.03%
Clustered tuners = 5.17%

## Slide 18: Conclusions
Cache tuning specializes system’s cache configuration to varying application requirements
Cache tuner must constitute minimal power, performance, and area overhead
We presented low overhead cache tuners
  Options: global, dedicated, and clustered tuners
  Scales to multiple cores
  Designers can select appropriate cache tuners based on design objectives
    Clustered tuners provide tradeoffs
  Analysis applicable to other tuning scenarios
Future work
  Evaluate cache tuners in up to 128 cores
  Incorporate lightweight communication network on cache tuner
    Independent of on-chip communication network

## Slide 19: Questions?