## Slide 1
A Single-Pass Cache Simulation Methodology for Two-level Unified Caches
+ Also affiliated with NSF Center for High-Performance Reconfigurable Computing
Wei Zang and Ann Gordon-Ross+
University of Florida Department of Electrical and Computer Engineering
This work was supported by the National Science Foundation (CNS-0953447) and (ECCS-0901706)

## Slide 2: Introduction
Caches are a good candidate for system performance and energy optimization
Different applications have vastly different cache requirements
  Configurable cache parameters: total size, line size, associativity
Cache tuning
  Determine appropriate cache parameters (cache configuration) to meet optimization goals
  Difficult to determine the best cache configuration given very large design spaces for highly configurable caches
line size
associativity
size

## Slide 3: Simulation-Based Cache Tuning
  Cache tuning at design time via simulation
  Performed by the designer
  Typically iterative simulation using exhaustive or heuristic methods
Instruction Set Simulator
Embedded
Application
Simulating
with c1
Miss rate
with c1
. . .
. . .
. . .
Simulating
with c2
Simulating
with c3
Simulating
with cn
Miss rate
with c2
Miss rate
with c3
Miss rate
with cn
Best c3 for optimization goals
…very time
consuming (setup
and simulation time)…
C1,C2,C3,…,Cn are the
n cache configurations
in design space

## Slide 4: Single-Pass Cache Tuning
  Simultaneously evaluate multiple cache configurations during one execution
  Trace-driven cache simulation
    Use memory reference trace
Generate trace file via a single functional simulation
Embedded
Application
Single-pass
trace-driven
cache simulation
Miss rate
with c3
Miss rate
with c1
Miss rate
with c2
Miss rate
with cn
. . .
. . .
Speedup simulation time
Best c3 for optimization goals

## Slide 5: Previous Works on Single-Pass Simulation
  Stack-based algorithm
  Stack data structure stores access trace
  Simple data structures, amenable to hardware implementation
  Tree-based algorithm
  Decreased simulation time
  Complex data structures, more storage requirements
Limitation
. . .
. . .
Processor
L1 cache
Main Mem
Processor
L1 I cache
Main Mem
L2 I cache
L2 D cache
L1 D cache
T-SPaCS
(Zang and Gordon-Ross, 11)
Processor
L1 I cache
Main Mem
L2 U cache
L1 D cache
Popular
U-SPaCS

## Slide 6: Single-level Cache Simulation
  Stack-based single-pass trace-driven cache simulation for single-level caches
One cache configuration in design space:
block size = 4 (22), number of cache sets = 8 (23)
Stack
Trace addresses
001 111 10
010 111 10
101 010 00
111 111 01
110 101 00
010 111 10
Block offset
Index
tag
(001) 111 10
001 111 10
010 111 10
101 010 00
111 111 01
110 101 00
010 111 10
Processing address
No previous access in stack
Search stack
Compulsory miss
Stack update
(001) 111 10

## Slide 7: Single-level Cache Simulation
  Stack-based single-pass trace-driven cache simulation for single-level caches
One cache configuration in design space:
block size = 4 (22), number of cache sets = 8 (23)
Stack
Trace addresses
001 111 10
010 111 10
101 010 00
111 111 01
110 101 00
010 111 10
Block offset
Index
tag
(010) 111 10
010 111 10
101 010 00
111 111 01
110 101 00
010 111 10
Processing address
No previous access in stack
Search stack
Compulsory miss
(001) 111 10
Stack update
(010) 111 10

## Slide 8: Single-level Cache Simulation
  Stack-based single-pass trace-driven cache simulation for single-level caches
One cache configuration in design space:
block size = 4 (22), number of cache sets = 8 (23)
Stack
Trace addresses
001 111 10
010 111 10
101 010 00
111 111 01
110 101 00
010 111 10
Block offset
Index
tag
(101) 010 00
101 010 00
111 111 01
110 101 00
010 111 10
Processing address
No previous access in stack
Search stack
Compulsory miss
(001) 111 10
(010) 111 10
Stack update
(101) 010 00

## Slide 9: Single-level Cache Simulation
  Stack-based single-pass trace-driven cache simulation for single-level caches
One cache configuration in design space:
block size = 4 (22), number of cache sets = 8 (23)
Stack
Trace addresses
001 111 10
010 111 10
101 010 00
111 111 01
110 101 00
010 111 10
Block offset
Index
tag
(111) 111 01
111 111 01
110 101 00
010 111 10
Processing address
No previous access in stack
Search stack
Compulsory miss
(001) 111 10
(010) 111 10
(101) 010 00
Stack update
(111) 111 01

## Slide 10: Single-level Cache Simulation
  Stack-based single-pass trace-driven cache simulation for single-level caches
One cache configuration in design space:
block size = 4 (22), number of cache sets = 8 (23)
Stack
Trace addresses
001 111 10
010 111 10
101 010 00
111 111 01
110 101 00
010 111 10
Block offset
Index
tag
(110) 101 00
110 101 00
010 111 10
Processing address
No previous access in stack
Search stack
Compulsory miss
(001) 111 10
(010) 111 10
(101) 010 00
(111) 111 01
Stack update
(110) 101 00

## Slide 11: Single-level Cache Simulation
  Stack-based single-pass trace-driven cache simulation for single-level caches
One cache configuration in design space:
block size = 4 (22), number of cache sets = 8 (23)
Stack
Trace addresses
001 111 10
010 111 10
101 010 00
111 111 01
110 101 00
010 111 10
Block offset
Index
tag
010 111 10
Processing address
(001) 111 10
(010) 111 10
(010) 111 10
(101) 010 00
(111) 111 01
(110) 101 00
Search stack
same block
(010) 111 10
(111) 111 01
Conflicts: blocks that map to the same cache set as processed address
Conflict evaluation: determine the config. that results in a hit
Conflicts # = 1
cache associativity >= 2, hit
Stack update

## Slide 12: Challenges in Unified L2 Cache Analysis
U-SPaCS targets exclusive hierarchy
  Storage space and simulation time efficiency (T-SPaCS)
L1 instruction (I) and data (D) caches share L2 cache -> introduces interference in the unified (U) L2 cache
  M L1 I cache configurations and N L1 D cache configurations generates M∙N unique eviction orderings
  Efficiently maintain and process the orderings for large design space
Trace | L1 I cache (2-way) | LI D cache (1-way) | L2 cache (2-way)
I1 | I1 |  | 
I2 | I2 I1 |  | 
D1 | I2 I1 | D1 | 
D2 | I2 I1 | D2 | D1
I3 | I3 I2 | D2 | I1 D1
I4 | I4 I3 | D2 | I2 I1
D1 | I4 I3 | miss | miss
Interdependency
Depends on relative eviction ordering of the two L1 caches

## Slide 13: U-SPaCS Overview
Execute
application
Access trace file
T[N]
:
T[t]
:
T[3]
T[2]
T[1]
U-SPaCS
B: block size
Accumulated
L1 I & D cache misses
L2 cache misses &
write-backs
for all cache config.
L1 I cache config.
L1 D cache config.
L2 U cache config.
Stack update
L1 analysis
Instruction T[t]
L2 analysis
L1 miss
Data
T[t]
L1 analysis
L2 analysis
Stack update
L1 miss
L2 analysis
L2 analysis

## Slide 14: Eviction Order Recording
L2 cache storage depends on relative eviction ordering
Stack maintains cache access ordering of unique addresses
  Not sufficient to determine eviction ordering
Explicitly record eviction ordering
Instruction (data) stack
Block address X
 |  | E |  | 
For each c1_inst(c1_data)
c1_inst: L1 I cache configuration
c1_data: L1 D cache configuration
S2: # of sets in L2 cache
Eviction time array
E: The time when X is evicted from L1 I (D) cache with L1 config. c1_inst(c1_data)
E=‘0’: X is still in L1, not evicted yet
Process block address A:
L2 analysis
A’s S2 conflicts that are evicted to L2 later than old A’s eviction (E of conflicts > E of A) determine A’s L2 hit/miss

## Slide 15: U-SPaCS Processing Example
-> 8
L2 cache (S = 23, W = 2)
L1 I cache (S = 22, W = 2)
L1 D cache (S = 23, W = 1)
Trace
D1(010)
I1(010)
I2(110)
D2(010)
D3(010)
I1(010)
I3(010)
I4(110)
I Stack
D Stack
1
2
3
5
7
8
4
6
D1(010)
I1(010)
I2(110)
I3(010)
D2(010)
I4(110)
D3(010)
D1(010)
I1(010)
I2(110)
I3(010)
D2(010)
I4(110)
D3(010)
I1(010)
Trace order 1: Process D1(010)
Compulsory miss
Trace order 2: Process I1(010)
Compulsory miss
Trace order 3: Process I2(110)
Compulsory miss
Conflicts for S1: I1(010)
W1 = 2, no eviction
-> 0
-> 0
-> 0
-> 0
Trace order 4: Process I3(010)
Compulsory miss
Conflicts for S1: I2(110) I1(010)
W1 = 2, I1(010) is evicted
-> 4
-> 0
Trace order 5: Process D2(010)
Compulsory miss
Conflicts for S1: D1(010)
W1 = 1, D1(010) is evicted
-> 5
-> 0
Trace order 6: Process I4(110)
Compulsory miss
Conflicts for S1: I3(010) I2(110) I1(010)
W1 = 2, I2(110) is evicted
-> 6
-> 0
Trace order 7: Process D3(010)
Compulsory miss
Conflicts for S1: D2(010) D1(010)
W1 = 1, D2(110) is evicted
-> 7
-> 0
Trace order 8: Process I1(010)
Conflicts for S1: I4(110) I3(010) I2(110)
W1 = 2, L1 miss, I3(010) is evicted
Conflicts for S2:
From I Stack: I3(010)->0
From D Stack: D3(010)->0 D2(010)->7; D1(010)->5
Eviction time of I1(010) is 4
Eviction time > 4
W2 = 2, L2 miss

## Slide 16: Special Case - Occupied Blank Labeling
I7
I6
I1
I2
I3
I4
I5
Trace
I4
I6
I2
I3
I2
I1
I5
I7
I5
L2 set (4 ways)
L2 set (4 ways)
L1 set (2 ways)
I Stack
Access I5
BLK
Occupied blank (invalid due to exclusive)
(fetching I2 evicts I6 that maps to a different L2 set)
From cache: miss in L1/L2
Analysis from Stack:
Conflicts for S2 : I2->0 I1->7 I3->5 I4->4 (no conflicts in D Stack)
Eviction time > 3; L2 hit
I5->3
Solution: occupied blank labeling
I4
I6
I2
I3
I2
I1
I5
I7
I5
Access I2
Hit in L2
I5
Inaccurate! L2 conflicts should count BLK
S1 < S2
-> 0
2
3
4
6
8
9
5
7
1
-> 3
-> 0
-> 4
-> 0
-> 5
-> 9
-> 0
-> 6
-> 0
-> 7
-> 0
-> 8
-> 0
-> 0
-> 0

## Slide 17: Data Address Processing
Similar to instruction address processing
Additional dirty data write-back counting
  Writing a dirty cache block avoids previous writing to memory
  #of write-back = # of total writes - # of write avoids
D stack
D1
1 | 0 | 1 |  | 1
0 | 0 | 0 |  | 0
0 | 1 | 1 |  | 0
1 | 0 | 1 |  | 0
0 | 0 | 1 |  | 1
Bit array for dirty status indication
D2
D3
D4
D5
Now process D4, during stack update:
Remove the old D4, and push new D4 on top
For each c_hier(c1_inst, c1_data, c2)
‘1’: dirty; ‘0’: clear
c_hier : cache hierarchy configuration
c1_inst: L1 I cache configuration
c1_data: L1 D cache configuration
c2: L2 cache configuration
D4 is a write:
Bit array of old D4
Bit array of new D4 (All dirty)
1 | 0 | 1 |  | 0
1 | 1 | 1 |  | 1

## Slide 18: Data Address Processing
Similar to instruction address processing
Additional dirty data write-back counting
  Writing a dirty cache block avoids previous writing to memory
  #of write-back = # of total writes - # of write avoids
D stack
D1
1 | 0 | 1 |  | 1
0 | 0 | 0 |  | 0
0 | 1 | 1 |  | 0
1 | 0 | 1 |  | 0
0 | 0 | 1 |  | 1
Bit array for dirty status indication
D2
D3
D4
D5
Now process D4, during stack update:
Remove the old D4, and push new D4 on top
For each c_hier(c1_inst, c1_data, c2)
‘1’: dirty; ‘0’: clear
c_hier : cache hierarchy configuration
c1_inst: L1 I cache configuration
c1_data: L1 D cache configuration
c2: L2 cache configuration
D4 is a read:
Bit array of old D4
Bit array of new D4
1 | 0 | 1 |  | 0
1 | 0 | 0 |  | 0
This c_hier results in L2 miss

## Slide 19: Experiment Setup
Design space
  L1 I & D caches: cache size (2k8k B); block size (16B64B); associativity (direct-mapped4-way)
  L2 cache: cache size (16k64k B); block size (16B64B); associativity (direct-mapped4-way)
  2,187 configurations
24 benchmarks from EEMBC, Powerstone, and MediaBench
Modif SimpleScalar’s ‘sim-fast’ to generate cache access traces
Implement U-SPaCS in C
Modify ‘Dinero’ to simulate exclusive hierarchy cache
  Produces the exact miss and write-back rates for comparison
U-SPaCS results are 100% accurate for all configurations!
Cache tuning using U-SPaCS determines optimal cache configuration!

## Slide 20: Simulation Time Efficiency
U-SPaCS’s (single-pass evaluation) vs. Dinero’s (iterative evaluation) simulation times for entire design space
Chart: Speedup
| bcnt | bilv | blit | brev | fir | A2TIME01 | AIFFTR01 | AIFIRF01 | AIIFFT01 | BaseFP01 | BITMNP01 | CACHEB01 | CANRDR01 | IDCTRN01 | IIRFLT01 | PNTRCH01 | PUWMOD01 | RSPEED01 | TBLOOK01 | TTSPRK01 | epic | mpeg2decode | pegwitencode | jpegencode | average
 | 72.7227 | 34.2299 | 61.8074 | 71.6013 | 61.382 | 12.4577 | 22.1359 | 58.004 | 21.5703 | 45.5375 | 34.7436 | 29.8019 | 49.2815 | 63.1837 | 13.4377 | 52.6212 | 51.9885 | 46.7008 | 34.629 | 24.8114 | 30.8836 | 46.8774 | 12.8507 | 26.4758 | 40.8223
Max 72X
Avg 41X

## Slide 21: Analysis of Speedup Variation
Chart: Logarithmic-scaled access trace length
| 1.9884E7 | 1.9949567E7 | 2.1413747E7 | 3.3028288E7 | 3.327614E7 | 3.660593E7 | 4.2548784E7 | 4.3960851E7 | 4.5400147E7 | 4.9936494E7 | 5.2148246E7 | 5.4340142E7 | 5.6553312E7 | 5.8134282E7 | 8.0063116E7 | 8.1347912E7 | 9.0403534E7 | 1.12371259E8 | 1.27967548E8 | 1.4294017E8 | 2.14284742E8 | 3.03600747999997E8 | 4.39712604999997E8 | 9.42730142E8
Dinero simulation time (s) | 9615.62 | 10126.8 | 10098.49 | 17277.76 | 16464.78 | 18301.01 | 20710.64 | 22853.95 | 22280.77 | 24850.44 | 25891.53 | 25192.34 | 27478.95 | 24988.86 | 41023.79 | 41589.44 | 45809.44 | 55609.55 | 63909.34 | 68919.02 | 96940.22 | 151302.66 | 223110.07 | 471088.49
SPUC simulation time (s) | 346.49 | 214.53 | 283.54 | 1373.51 | 339.7 | 599.94 | 1536.18 | 423.11 | 288.45 | 1829.01 | 505.62 | 330.81 | 1085.64 | 787.93 | 675.78 | 1894.91 | 2034.2 | 1014.48 | 962.04 | 1951.72 | 2060.25 | 4236.72 | 3462.6 | 7261.87
SPUC's speedup | 27.7515 | 47.2046 | 35.6158 | 12.5793 | 48.4686 | 30.5047 | 13.4819 | 54.0142 | 77.2431 | 13.5868 | 51.2075 | 76.1535 | 25.3113 | 31.7146 | 60.7058 | 21.948 | 22.5196 | 54.8158 | 66.4311 | 35.3119 | 47.0526 | 35.7122 | 64.4343 | 64.8715
Linearly increase
Variation
U-SPaCS simulation time (s)
U-SPaCS speedup
Dinero simulation time (s)

## Slide 22: Analysis of Speedup Variation
Chart: Speedup
| 0.000252897797649676 | 0.0318553528338702 | 0.148442699109569 | 0.181768564914956 | 1.251681719062123 | 1.370352875815572 | 1.3837667484631 | 1.982366063211462 | 2.541463571226148 | 2.549650994497833 | 2.559578989597877 | 3.353669770022963 | 4.784142076367106 | 4.817926446127625 | 6.494546281601111 | 9.271448052142407 | 9.662705137011481 | 10.18785886031562 | 12.83742176947299 | 16.04065922915342 | 17.30924306547389 | 27.36617236423329 | 29.71902857914089 | 34.14510432690631
 | 77.2431 | 76.1535 | 64.8715 | 64.4343 | 60.7058 | 35.3119 | 66.4311 | 54.8158 | 54.0142 | 51.2075 | 48.4686 | 47.2046 | 47.0526 | 35.6158 | 35.7122 | 30.5047 | 25.3113 | 31.7146 | 27.7515 | 22.5196 | 21.948 | 12.5793 | 13.5868 | 13.4819
Chart: 
| 4.21309284059332E-9 | 5.66060354733684E-5 | 0.000743613819372377 | 0.00155329098056824 | 0.00429860507397145 | 0.00571155193494329 | 0.0116727690445978 | 0.0170833397969585 | 0.0202657924515832 | 0.02142771386408 | 0.0250543777097874 | 0.0424459336517265 | 0.0822793364740889 | 0.0938075389823447 | 0.123800802174583 | 0.182772653386152 | 0.190319150598772 | 0.313601361270539 | 0.341537881187439 | 0.596950484972143 | 0.657750631939442 | 2.322378610852757 | 2.636847159490577 | 2.801396102699822
 | 77.2431 | 76.1535 | 64.8715 | 64.4343 | 60.7058 | 66.4311 | 54.8158 | 54.0142 | 48.4686 | 51.2075 | 47.2046 | 47.0526 | 35.3119 | 35.6158 | 35.7122 | 30.5047 | 31.7146 | 25.3113 | 27.7515 | 22.5196 | 21.948 | 12.5793 | 13.5868 | 13.4819
Product of the average L1 cache miss rate and the average stack size
Outlier
High average L1 cache miss rate
Product of the square of the average L1 cache miss rate and the average stack size
High importance placed on L1 cache miss rate
All benchmarks follow decreasing tread

## Slide 23: Conclusions
U-SPaCS simulates an exclusive two-level cache hierarchy with a unified L2 cache in a single pass
U-SPaCS’s cache miss rates and write-back rates are 100% accurate for all cache configurations
  U-SPaCS achieves an average 41X simulation time speedup as compared to iterative simulation
Our ongoing work
  Extend U-SPaCS to support multi-core architectures
  Implement U-SPaCS in hardware for dynamic cache tuning