## Slide 1
An Automated Hardware/Software Co-Design
Flow for Partially Reconfigurable FPGAs
Ann Gordon-Ross
Associate Professor, University of Florida Department of Electrical and Computer Engineering
Shaon Yousuf*
University of Florida Department of Electrical and Computer Engineering *Currently affiliated with Intel Corporation

## Slide 2: Efficient Embedded System Design
Modern SRAM-based FPGAs provide partial reconfiguration (PR)
  Reconfigures isolated FPGA regions
    Partially reconfigurable region (PRRs)
  Only interrupts execution in reconfigured PRR
T1
T2
T3
T4
FPGA Fabric
PRR 1
PRR 2
PR enables efficient embedded system design
  Multiplex mutually exclusive application tasks in PRRs
    Reduces system area, memory, power requirements
Application Tasks
T1, T2, T3 required -
Load T1 to PRR1,
load T2 to PRR2,
Load T3 to PRR 3
T1, T2, T4 required -
load T4 to PRR3, T1 and T2 uninterrupted
PRR 3
T4, T5, T6 required
load T5 to PRR1, load T6 to PRR 2,
T4 uninterrupted
T5
T6
Time S1
Time S2
Time S3
T1
running
T2
running
T4
running
Notes: Time(min): 1:30
Total(min): 1:30

## Slide 3: Efficient Embedded System Design
Cutting edge PR-capable FPGAs can also contain software processors
  Enables designing hardware/software (HW/SW) hybrid systems
    Tasks execute in software and/or hardware
    Further reduces area requirements
  Designing hybrid systems is complex
    Difficult to leverage PR benefits effectively – known as a HW/SW co-design problem
T1
T2
T3
T4
FPGA Fabric
Software Processor
PRR 2
Application Tasks
T1, T2, T3 required -
T1 and T2 runs in software,
Load T3 to PRR 2
T1, T2, T4 required –
T1 and T2 still running in software,
load T4 to PRR2
T4, T5, T6 required
T5 and T6 runs in software,
T4 uninterrupted
T5
T6
Time S1
Time S2
Time S3
T1 & T2
running
T4
running
T5 & T6
running
Area Savings
Notes: Time(min): 1:30
Total(min): 3:00

## Slide 4
Traditional HW/SW Co-design for PR Systems
HW/SW co-design of PR systems requires specialized design flow
  HW/SW PR partitioning allocates tasks into software and hardware, and allocates/maps hardware tasks into one or more PRRs
  PR design floorplanning determines physical placement of PRRs and PRR boundary communication interfaces (partition pins)
  Place and route, and final bitstream generation follows
PR partitioning and PR floorplanning are performance critical steps
  Chosen PR partition affects resource requirements and number of reconfigurations required (reconfiguration time)
  PR floorplan directly affects overall design speed (clock frequency)
HW/SW PR Partitioning
Application
Tasks
PR design Floorplanning
Chosen
HW/SW PR partition
  Performance critical steps
Place and Route Design
Generate Final
Design
Bitstreams
Notes: Time(min): 1:00
Total(min): 4:00

## Slide 5: HW/SW PR Partitioning Challenges
Many possible PR partitions
  Partition A requires more PRRs = more hardware requirements
  Partition B requires more reconfigurations = more reconfiguration time
  Challenge: Choose PR partition that meets system designer goals wrt hardware requirements and reconfiguration time tradeoff
T1
T2
T3
T4
T5
FPGA Hardware
HW Tasks partitioned into 2 PRRs
FPGA Software
PRR 2
T2
PRR 1
T1
SW Processor
T3,T4,T5
Partition B
T3
T4
T5
T1
T2
FPGA Hardware
HW Tasks partitioned into 1 PRRs
FPGA Software
PRR 1
T3, T4, T5
SW Processor
T1, T2
Partition A
Notes: Time(min): 0:30
Total(min): 4:30

## Slide 6: PR Design Floorplanning Challenges
Many possible PRR and partition pin floorplans
  Each floorplan has different total wire length and affects design clock frequency
    Example - Floorplan A with less wire length is faster that Floorplan B
  FPGA resource and clocking resource locations, and distance from input/output (I/O) interfaces also affects design clock frequency
  Challenge – Find PR design floorplan that meets system designer goals wrt to clock frequency
HW/SW PR partition A Chosen
Hardware Allocation – T1, T2
Software Allocation –
T3, T4, T5
PR Design Floorplanning
Requires more total wire length than Floorplan A
FPGA Fabric
FPGA Fabric
Partition A: Floorplan A
HW PRR 2
T2
SW Processor
T3,T4,T5
HW PRR 1
T1
Partition A: Floorplan B
SW Processor
T3,T4,T5
HW PRR 1
T1
HW PRR 2
T2
Partition Pins
Notes: Time(min): 0:30
Total(min): 5:00

## Slide 7
Design Automation for HW/SW Co-design
We present
  Design Automation for Partial Reconfiguration (DAPR) design flow to aid embedded system designers with HW/SW co-design challenges
  Performs automated HW/SW PR partitioning
    Automatically explores design space using an exhaustive search
    Designer chooses HW/SW PR partition that meets required goals
  Performs automated floorplanning on chosen HW/SW PR partition
    Automatically explores design space using a simulated annealing-based heuristics
    Leverages vendor tools to automatically output final design bitstreams
Determines PR partitions with reconfiguration time vs. area requirement tradeoffs
Works towards improving the clock frequency of the PR partition
DAPR Design Flow
Automated Partitioning
Automated Floorplanning
Final
Design
Bitstreams
Application
Tasks
Chosen
HW/SW PR partition
Notes: Time(min): 1:00
Total(min): 6:00

## Slide 8
Overview of Contributions
Automated design flow for efficient HW/SW PR co-design of PR systems
  Automated exhaustive search-based methodology of HW/SW PR partitions
    Partitions tradeoff reconfiguration time vs. area requirements
    Total system execution time for partitions is also reported
  Automated simulated annealing-based PR design floorplanning methodology
    Improves clock frequency to approximately 10% of the highest achievable clock frequency between 12-20 iterations on average
    Supports PR-capable Virtex-4, 5, 6, and 7 devices
      Generalized, thus easily extendable to any PR-capable device
DAPR design flow benefits
  Simple and holistic PR design flow that requires minimal design intervention
  Makes PR benefits easily attainable and amenable to designers
Notes: Time(min): 1:00
Total(min): 7:00

## Slide 9: DAPR’s Initial Analysis
  PR system design is modularized in nature
  Application divided into tasks
  Application task flow graph represents application functionality
  PR systems change during runtime
  Can have multiple task flow graphs (configurations) [Vipin et al. 2013]
T1
T2
T3
T4
T1
T5
Configuration 0
T1
T4
T3
T2
T1
T5
Configuration 1
T1
T2
T3
T4
Modularized Application Tasks
T5
Notes: Time(min): 0:30
Total(min): 7:30

## Slide 10: DAPR’s Initial Analysis
  To evaluate each configurations performance we define
  Tii – List of application tasks
  COi – List of tasks required in configuration i
  RRi -Task i’s resource requirements
    Estimated from HDL synthesis using vendor tools
  TRi - Task i’s reconfiguration time
    Estimated from number of frames required to reconfigure task
    Frames is the smallest addressable unit of an FPGA
    Reconfiguration time corresponds to total number of frames multiplied by device reconfiguration speed
  CIi - Task i’s software and hardware execution times
    Estimated by calculating total mathematical operations in a task (addition, subtraction, multiplication, division)
    Multiplied by operation’s HW/SW clock cycle latency
    Total clock cycle requirements correspond to execution times
Notes: Time(min): 0:30
Total(min): 8:00

## Slide 11
  HW/SW PR Partitioning Methodology
Modularized
Application
Configuration List, COi
Estimate Ti RRi, TRi, and CIi
HW/SW PR Partitioning Algorithm
HW/SW partitions and performance results
  Leverages configuration list and modularized application
  Determines Ti,RRi, TRi, and CIi performance parameters
  HW/SW PR algorithm generates all possible HW/SW PR partitions and corresponding partitions performance results
  Resource requirements, reconfiguration time, and HW/SW execution time reported
  System designer analyzes results, selects Chosen HW/SW PR partition
  Chosen HW/SW PR partition undergoes DAPR’s SA-based PR floorplanning
Analyze and select Chosen HW/SW partition
Notes: Time(min): 1:00
Total(min): 9:00

## Slide 12: Automated Floorplanning Algorithm
  Iteratively improves HW/SW PR partition’s floorplan
  Leverages simulated annealing (SA)-based algorithm
  PRR floorplan is improved first
    PRR floorplan changes have largest affect on design performance
  Partition pin floorplan is improved over last few iterations
  DAPR SA-based algorithm overview
  Evaluates PRR floorplan using an improved perturbation function
    New operation changes floorplan starting locations
  Evaluates partition pin floorplan with a new perturbation function
    Tailored specifically for partition pin placement exploration
Notes: Time(min): 0:30
Total(min): 9:30

## Slide 13: DAPR SA-based PRR Floorplanning
  Typical PR design floorplanning methods bounds static regions
  Static region routing constrained to bounded region
  Floorplanning performed considering static region as a PRR
  DAPR SA-based PRR floorplanning allows unbounded static regions
  Relaxes static region routing to reveal faster clock frequency designs
  New perturbation function enables unbounded static regions
    Floorplan starting locations changed after all PRR permutations is satisfied
PRR 1
PRR 3
Static
Region
PRR 2
PRR 4
Bounded floorplan
PRR 1
PRR 3
Static Region
PRR 2
PRR 4
Unbounded Floorplan A
Static Region
PRR 1
PRR 3
Static Region
PRR 2
PRR 4
Unbounded Floorplan B
Static Region
PRR 1
PRR 3
Static Region
PRR 2
PRR 4
Unbounded Floorplan C
Different PRR floorplan starting locations
Notes: Time(min): 0:30
Total(min): 9:30

## Slide 14: DAPR SA-based Partition Pin Floorplanning
PRR
  Partition pin floorplan is represented as list, P = {1,2,3 …., n}
  List number represents partition pin
  List index represents partition pin placement with respect to neighbors
  Improves partition pin floorplan iteratively with a novel perturbation function tailored for partition pin floorplanning
  OP1: Randomly place partition pins around PRR
  OP2: Switch adjacent input pin placements
  OP3: Switch adjacent output pin placement
  OP4: Switch adjacent input and output pins
Notes: Time(min): 0:30
Total(min): 10:00

## Slide 15
  DAPR Design Flow Evaluation
  Experimental Setup
  Software
    HW/SW PR partitioning algorithm written in PERL
    Xilinx ISE 14.7
  Hardware
    Virtex-5 LX110T FPGA
    4rth generation Intel® Core™ 7 2.5 GHz CPU and 8 GB of RAM
  Test design
  JPEG encoding/decoding application
  Next slides present
  COi, RRi, TRi, CIi estimations
  Maximum resource requirements, reconfiguration time, and software execution time results
Notes: Time(min): 0:20
Total(min): 10:20

## Slide 16
  JPEG CODEC Configurations
  Two configurations
  Configuration A – JPEG encoding process
  Configuration B – JPEG decoding process
  All tasks change between configurations
  Each configuration will have different requirements for each HW/SW PR partition
    Total resource requirements, reconfiguration time, and execution time will be different
  Enables accurate analysis of our HW/SW PR partitioning methodology
Notes: Time(min): 0:40
Total(min): 11:00

## Slide 17
  JPEG CODEC Resource Requirements
 | Resource requirements, RRi |  | 
Task List | CLBs | DSPs | BRAMs
RGB2YCbCR and FDCT | 406 | 7 | 5
YCbCrtoRGB and IDCT | 400 | 7 | 5
Run Length Encoding | 42 | 0 | 2
Run Length Decoding | 42 | 0 | 2
Huffman Encoder | 280 | 1 | 2
Huffman Decoder | 350 | 1 | 2
Byte Stuffer and header encoder | 14 | 0 | 1
Byte Stripper and header decoder | 14 | 0 | 1
Quantization | 14 | 2 | 3
Dequantization | 14 | 2 | 3
Zigzag | 14 | 0 | 2
Reorder | 14 | 0 | 2
Notes: Time(min): 0:20
Total(min): 11:20

## Slide 18
  JPEG CODEC Reconfiguration Times
Device reconfiguration speed is approximately 234MB/s [Liu et al 2009]
Task List | Reconfiguration time, TRi (Frames)
RGB2YCbCR and FDCT | 1650
YCbCrtoRGB and IDCT | 1600
Run Length Encoding | 480
Run Length Decoding | 480
Huffman Encoder | 1000
Huffman Decoder | 1100
Byte Stuffer and header encoder | 100
Byte Stripper and header decoder | 100
Quantization | 170
Dequantization | 170
Zigzag | 120
Reorder | 120
Notes: Time(min): 0:20
Total(min): 11:40

## Slide 19
  JPEG CODEC Execution Times
  SW runs on VAPRES Micro Blaze softcore processor
  Clock cycles – Add =1, subtract =1, divide = 3, and multiply = 34 *
  HW runs on FPGA
  Clock cycles – Add =1, subtract =1, divide = 1, and multiply = 1*
* Taken from Xilinx DS100 2009
 | Execution times, CIi | 
Task Name | SW Execution (cycles) | HW Execution (cycles)
RGB2YCbCR and FDCT | 40,000 | 10,000
YCbCrtoRGB and IDCT | 42,000 | 10,000
Run Length Encoding | 10,000 | 2,000
Run Length Decoding | 10,000 | 2,000
Huffman Encoder | 25,000 | 10,000
Huffman Decoder | 30,000 | 10,000
Byte Stuffer and encoder | 20 | 20
Byte Stripper and header decoder | 20 | 20
Quantization | 40 | 40
Dequantization | 40 | 40
Zigzag | 40 | 40
Reorder | 40 | 40
Notes: Time(min): 0:20
Total(min): 12:00

## Slide 20
  Results: HW/SW Partition Exploration
Partitions with low resource requirement and reconfiguration time
Notes: Time(min): 1:00
Total(min): 13:00

## Slide 21
  Results: HW/SW Partition Exploration
Partitions with low total execution time
Notes: Time(min): 1:00
Total(min): 14:00

## Slide 22
  Results: HW/SW PR Partition Selection
Example system designer requirements for both configurations
  Resource requirements 12,000 slices, reconfiguration time 9000 frames, and total system execution 25,000 cycles
  Choose any HW/SW PR partition between 1-1000
HW/SW PR partitions that meet system designer goals
Notes: Time(min): 1:00
Total(min): 16:00

## Slide 23
Due to simulated annealing’s initial random exploration, 3 different floorplan runs are shown
Solution improves with successful iterations (highlighted circle)
Growth rate quickly levels off to within 1.8 % of the highest achievable within average of 20 iterations
  Results: JPEG Codec Design Space Exploration
Notes: Time(min): 1:00
Total(min): 17:00

## Slide 24: Conclusions and Future Direction
We presented the DAPR design flow
  Determines HW/SW PR partitions that tradeoff resource requirements and reconfiguration time
  Designers choose a HW/SW PR partition that satisfy system design goals
  Leverages a novel simulated annealing based algorithm to improve the clock frequency of the HW/SW PR design partition
The DAPR design flow alleviates intricacies involved in HW/SW co-design of PR-based embedded systems by automation
  DAPR design flows makes PR design more accessible and amenable to a wide range of system designers
  Future directions
  Improve DAPR design flows HW/SW PR partitioning methodology’s estimation technique for hardware/software execution time calculation
    Leverage an application profiler
  Explore techniques to improve DAPR design flows PR design floorplanning
  Enhance portability of DAPR design flow to Altera Devices
Notes: Time(min): 1:00
Total(min): 18:00

## Slide 25
QUESTIONS?
This work was supported in part by the I/UCRC Program of the National Science Foundation under Grant No. EEC-0642422. We also gratefully acknowledge tools provided by Xilinx.