## Slide 1: Realizing Closed-loop, Online Tuning and Control for Configurable-Cache Embedded Systems: Progress and Challenges
Islam S. Badreldin*, Ann Gordon-Ross*, Tosiron Adegbija§, and Mohamad Hammam Alsafrjalani+
Department of Electrical & Computer Engineering
*University of Florida, §University of Arizona, +University of Miami
{ibadreldin,anngordonross}@ufl.edu, tosiron@email.arizona.edu, alsafrjalani@miami.edu

## Slide 2: Introduction and Motivation
Embedded systems have become ubiquitous
  Stringent design constraints: energy, performance, Quality of Experience (QoE) expectations, cost
  Increasingly complex memory and compute requirements
  Must operate in unknown and changing environments, and demands
    Application characteristics
    User expectations
  Feature complex heterogeneous processors to satisfy execution demands and diversity

## Slide 3: The Cache Subsystem
Caches can consume up to 50% of total processor power
  Cache optimization more important in heterogeneous multicore systems
  Caches must be adaptable to varying execution demands, environments, and user QoE expectations/feedback
    I.e., configurable caches
  Cache design space becomes extremely large when considering QoE expectations
    Cache tuning becomes more complex

## Slide 4: Configurable Caches

## Slide 5: Cache Tuning in Heterogeneous Cores
New dynamic cache tuning methods required
  When to reconfigure the cache
  Incorporating runtime time-varying user QoE expectations
  User-defined optimization metrics
  Data sharing, cache coherence, etc.
Impact of cache tuning on user experience
  Must not degrade user experience during cache tuning
Need online, closed-loop, user-aware cache tuning systems

## Slide 6: Overview of Cache Tuning Methods
Cache tuning
(Design space exploration)
Offline DSE
Online DSE
Heuristics
Analytical methods
Simulation-based
Subsetting
Eliminate DSE
Explore 1% of design space
Near-optimal configs
Static configs

## Slide 7: Problem Formulation
Set of n applications
Set of m possible cache configurations
Set of ki application phases per application ai
Energy-related optimization metric
Performance-related optimization metric
Pareto-optimal design
with ‘<‘ for some
& with ‘<‘ for some
Energy
Execution time
Pareto
optimal designs

## Slide 8: Online Cache Tuning and Control
Goal: continuously monitor and adapt to changing user and environment requirements
  Must be transparent to both user and application
  Need a feedback control system for self-monitoring and online adjustment
Requirements of a self-tuning cache system
  1. Monitor and collect information about system behavior
  2. Dynamically reconfigure tunable parameter values
  3. Determine when to change configurations in response to phase changes without incurring significant penalties
  4. Adapt to user QoE expectations; limit QoE degradation

## Slide 9: Proposed Ideal Self-Tuning Cache System
Notes: Controller (tuner): incorporates QoE awareness; phase-based statistical model (linear/non-linear adaptive filters)
Temporal execution data: consider history of execution statistics and performance metrics as time series
  No need to explicitly perform phase classification
  Operate at high temporal resolution while dynamically tuning interval
Plant (cache subsystem): single level, multilevel, multicore

## Slide 10: Challenges of Online Cache Tuning and Control
Avoiding QoE degradation due to DSE overheads
   use analytical and prediction-based models to limit the DSE to a few best options
Performing well even for applications that are unknown at design time
   use online adaptation and control to update the model data in real-time
Operating at an optimal tuning interval
   operate at high temporal resolution using online filtering while dynamically adjusting the tuning interval
Tracking variations in QoE expectations
   incorporate sensor values and historical data to directly predict best configurations given an estimated QoE expectation
Incorporating user feedback
   combine both intrusive and non-intrusive techniques to solicit user feedback to identify what the user considers a best configuration

## Slide 11: Conclusions
Efficient self-tuning caches critical for emerging resource-constrained computers
  May operate in unknown environments
  Wide variety of applications
  Different kinds of users may require different kinds of runtime tuning
Several challenges exist for realizing self-tuning cache that is transparent to both the user and the executing applications
  Minimizing DSE overheads
  Self-tuning for unknown applications
  Meeting user QoE expectations
  Etc.
Future work: explore proposed ideal architecture towards addressing the challenges
  Use an online, adaptive statistical model to predict best configuration given historical data, user feedback, sensor readings, etc.
  QoE-aware optimization, and dynamic adjustment of the tuning interval