## Slide 1
Exploring the Tradeoffs of Configurability and Heterogeneity in Multicore Embedded Systems
+ Also Affiliated with NSF Center for High-Performance Reconfigurable Computing
Tosiron Adegbija and Ann Gordon-Ross+
Department of Electrical and Computer Engineering
University of Florida, Gainesville, Florida, USA
This work was supported by National Science Foundation (NSF) grant CNS-0953447

## Slide 2: Introduction and Motivation
Ubiquitous embedded systems have diverse design challenges
  Design goals: cost, energy consumption, time-to-market, performance, etc.
  Design constraints: energy, area, real time, cost, etc.
  Tunable parameters: cache configuration, voltage, frequency, etc.
  Varying per-application parameter value requirements
  Specialize configuration to varying application characteristics (e.g., cache miss rates, instruction per cycle, etc.)
Multicore architectures increasingly common in embedded systems
  Alternatives to single-core architectures for achieving design goals
  Significantly complicates design challenges
Application 1
Application 2
Application 3
$
8 KB
direct-mapped
16B line size
1 GHz
clock
frequency
$
16 KB
2-way
32B line size
1 GHz
clock
frequency
$
32 KB
4-way
64B line size
2 GHz
clock
frequency

## Slide 3: Configuration Specialization
Specialize system configuration to specific application requirements
  Specialize for optimization goals: lowest energy, best performance, energy delay product (EDP), etc.
  E.g., cache tuning saves up to 60% of energy on average
    Balasubramonian’00, Zhang’03
Tuning determines the best configuration for each executing application
  Best/optimal configuration with respect to optimization goals
  Tuning evaluates potential configurations to determine best configuration
Energy
Possible configurations
best configuration
Energy
Possible configurations
best configuration
Application 1
Application 2
Energy
Possible configurations
best configuration
Application 3
Tuning
Tuning
Tuning
Configurations must be specialized each application.

## Slide 4: Homogenous Cores
Traditional homogeneous cores
  Identical configurations
  Severely inhibits specialization
Core1
Core2
Different cores with identical configurations
Remains the same throughout system lifetime
Homogeneous cores
Previous work showed that specialization has significant impact on energy consumption
  Limiting energy consumption is critical in embedded system
  Cache and core frequency are key energy components
    Our work focuses on cache and core frequency specialization
What are the methods for achieving specialization?

## Slide 5: Specialization Methods
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Different cores with different configurations
Remains same throughout system lifetime
Heterogeneous cores
Configurable homogeneous cores
Configurable heterogeneous cores
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Different cores with same configurations
Cores are tuned simultaneously
Configurations change dynamically
Different cores with different configurations,
Cores are tuned independently
Configurations change dynamically
Different methods have different design challenges and architecture options
Which specialization methods should designers use?

## Slide 6: Design Challenges – Large Design Space
Configuration Design Space
Number of configurations limited
to the number of cores
Number of configurations to explore grows exponentially with the number of cores
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Heterogeneous cores
Configurable homogeneous cores
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Configurable heterogeneous cores
Specialization potential

## Slide 7: Design Challenges – Large Design Space
Configuration design space
Scheduling applications to the best core
Scheduling to the best core AND determining the best configuration
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Heterogeneous cores
Configurable homogeneous cores
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Core1
Core2
Configurable heterogeneous cores
Determining the best configuration
Using a sub-optimal schedule or configuration wastes energy!

## Slide 8: Design Challenges – Limiting Tuning Overhead
Heterogeneous
cores
Configurable
homogeneous
cores
Configurable
heterogeneous
cores
Tuning overhead
Tuning overhead typically increases with specialization options
Energy
consumed during tuning
Energy
Possible configurations
best configuration
Tuning
Design space

## Slide 9: Design Challenges Heterogeneous Core Architectures
Main Memory
Processor
core 1
Data Cache
Instruction Cache
L1
Processor
core 2
Data Cache
Instruction Cache
L1
Different cores with different
configurations
Choosing the best core configurations
How disparate should the
configurations be?
Cores should be suitable for
a variety of applications.
Requires a priori analysis
E.g., core frequency, cache
configurations, issue queue,
reorder buffer, etc.

## Slide 10: Design Challenges Configurable Homogenous Core Architectures
Different cores with identical
configurations that change during
execution
When should the configurations change during execution?
Configurability of the cores/design space
Requires tuning hardware (e.g., power monitor to measure power, and tuner to determine best configuration and change configurations
Main Memory
Processor
core 1
Data Cache
Instruction Cache
L1
Processor
core 2
Data Cache
Instruction Cache
L1
Tuner
Power monitor

## Slide 11: Design Challenges Configurable Heterogeneous Core Architectures
Different cores with different
configurations that change during
execution
When should the configurations change during execution?
Configurability of the cores/design space
Requires tuning hardware (e.g., power monitor to measure power, and tuner to determine best configuration and change configurations
Main Memory
Processor
core 1
Data Cache
Instruction Cache
L1
Processor
core 2
Data Cache
Instruction Cache
L1
Tuner
Power monitor
Which configurations
should be different?

## Slide 12: Design Challenges - Summary
Heterogeneous cores
  Which configurations should be different?
    How different should the configurations be?
  How to determine the different configurations?
    Requires significant design time a priori analysis
Configurable homogeneous cores
  Imposes hardware overhead (e.g., tuner, power monitor, etc.)
  Imposes tuning overhead
  How often should the configuration change?
  How configurable should the cores be?
Configurable heterogeneous cores
  Intersection of heterogeneous and configurable homogeneous core challenges
  Significantly larger design space
Our work quantifies these architectural tradeoffs and provides insight for design decisions

## Slide 13: Experimental Setup
Evaluated heterogeneity and configurability with respect to core frequency and cache configurations
  Significant impact on system’s overall energy
    Nacul ’04
Energy delay product (EDP) as evaluation metric
  EDP = core_power * running_time2
  = core_power * (total_application_cycles/system_frequency)2
  Core_power: cache and core’s components (e.g., network interface units (NIU), peripheral component interconnect (PCI) controllers, etc.)
McPAT calculated power consumption
24 multi-programmed workloads from EEMBC and Mediabench benchmark suites

## Slide 14: Experimental Setup
Modeled configurable/heterogeneous cores using GEM5
  Modeled dual-core systems common in modern-day embedded systems
    Modified GEM5 to simulate heterogeneous cores
Dual-core systems and configuration |  |  |  | 
System | Cache size | Associativity | Line size | Clock frequency
Homogeneous | 32 Kbyte | 4 way | 64 byte | 2 GHz
Configurable | 16 – 32 Kbyte | 1 – 4 way | 16 – 64 byte | 1 – 2 GHz
Heterogeneous-1 | 16/32 Kbyte | 4 way | 64 byte | 1/2 GHz
Heterogeneous-2 | 8/16 Kbyte | 4 way | 64 byte | 800 MHz/1 GHz
Heterogeneous-3 | 8/32 Kbyte | 4 way | 64 byte | 800 MHz/2 GHz
Best average configuration
for all workloads after extensive
design time a priori analysis
Configuration selection options with
no extensive design time a priori analysis

## Slide 15: Experimental Setup
Experimental test scenarios | 
Name | Core descriptions
Test scenario 1 | Naively-scheduled Heterogeneous-1
Test scenario 2 | Optimally-scheduled Heterogeneous-1
Test scenario 3 | Configurable homogeneous
Test scenario 4 | Configurable heterogeneous
Highest EDP schedule
(worst-case EDP)
Lowest EDP schedule
Used exhaustive search to
determine best configurations

## Slide 16: Results - Homogenous Core System
Chart: EDP normalized to the homogeneous core system
| iirflt01-basefp01 | mpeg2encode-rspeed01 | tblook01-puwmod01 | puwmod01-mpeg2encode | canrdr01-tblook01 | g721decode-iirflt01 | g721decode-pntrch01 | tblook01-mpeg2encode | iirflt01-ttsprk01 | rspeed01-mpeg2decode | g721encode-mpeg2encode | aifftr01-mpeg2decode | g721encode-bitmnp01 | a2time01-cacheb01 | mpeg2decode-canrdr01 | pntrch01-basefp01 | mpeg2encode-iirflt01 | puwmod01-canrdr01 | tblook01-g721decode | puwmod01-djpeg | djpeg-bitmnp01 | bitmnp01-g721decode | canrdr01-aifftr01 | iirflt01-bitmnp01 | average | standard deviation
Test scenario 1 | 0.86528 | 0.86577 | 0.86497 | 0.86539 | 0.86495 | 0.86426 | 0.8638 | 0.86495 | 0.86869 | 0.88247 | 0.86426 | 0.88919 | 0.86426 | 0.86448 | 0.88245 | 0.86459 | 0.86526 | 0.86481 | 0.86426 | 0.90749 | 0.90997 | 0.86426 | 0.30511 | 0.86526 | 0.84776 | 0.11635
Test scenario 2 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.8642 | 0.86422 | 0.86376 | 0.8642 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.86421 | 0.8642 | 0.86422 | 0.86422 | 0.863 | 0.86537 | 0.86422 | 0.29654 | 0.8642 | 0.84054 | 0.11587
Test scenario 3 | 0.98324 | 0.72844 | 0.72844 | 0.72844 | 1 | 1 | 0.99947 | 1 | 0.72844 | 0.34311 | 1 | 0.72662 | 0.72844 | 0.72844 | 0.72844 | 1 | 0.99996 | 0.72844 | 0.99996 | 0.99907 | 0.99957 | 0.99999 | 0.34229 | 0.99988 | 0.84253 | 0.20151
Test scenario 4 | 0.72844 | 0.72844 | 0.72844 | 0.72844 | 0.72843 | 0.72844 | 0.72805 | 0.72843 | 0.72844 | 0.72844 | 0.72844 | 0.72662 | 0.72844 | 0.72844 | 0.72844 | 0.72843 | 0.72843 | 0.72844 | 0.72844 | 0.72741 | 0.72941 | 0.72844 | 0.24928 | 0.72843 | 0.70838 | 0.097788
Naively-scheduled Heterogeneous-1:
15% EDP savings
Optimally-scheduled Heterogeneous-1:
16% EDP savings
Configurable homogeneous:
16% EDP savings
Configurable heterogeneous:
29% EDP savings
Configurable | 16 – 32 Kbyte | 1 – 4 way | 16 – 64 byte | 1 – 2 GHz
Heterogeneous-1 | 16/32 Kbyte | 4 way | 64 byte | 1/2 GHz

## Slide 17: Results
Optimally-scheduled Heterogeneous-1, -2, and -3 compared to homogeneous core
Chart: EDP normalized to the homogeneous core system
| iirflt01-basefp01 | tblook01-puwmod01 | puwmod01-mpeg2encode | g721decode-iirflt01 | g721decode-pntrch01 | iirflt01-ttsprk01 | rspeed01-mpeg2decode | aifftr01-mpeg2decode | g721encode-bitmnp01 | a2time01-cacheb01 | pntrch01-basefp01 | mpeg2encode-iirflt01 | tblook01-g721decode | puwmod01-djpeg | bitmnp01-g721decode | canrdr01-aifftr01 | average | standard deviation
Heterogeneous-1 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.86376 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.86421 | 0.8642 | 0.86422 | 0.863 | 0.86422 | 0.29654 | 0.84054 | 0.14189
Heterogeneous-2 | 1.0971 | 1.0967 | 1.0972 | 1.0958 | 1.0952 | 1.1014 | 1.1189 | 1.1274 | 1.0958 | 1.0961 | 1.0962 | 1.0971 | 1.0958 | 1.1506 | 1.0958 | 0.38686 | 1.0749 | 0.17991
Heterogeneous-3 | 0.83706 | 0.83707 | 0.83707 | 0.83706 | 0.83661 | 0.83706 | 0.83699 | 0.83707 | 0.83707 | 0.83707 | 0.83705 | 0.83705 | 0.83706 | 0.83363 | 0.83706 | 0.28722 | 0.815 | 0.1374
Heterogeneous-1:
16% EDP savings
Heterogeneous-2:
7% EDP increase
Heterogeneous-3:
19% EDP savings
Heterogeneous-1 | 16/32 Kbyte | 4 way | 64 byte | 1/2 GHz
Heterogeneous-2 | 8/16 Kbyte | 4 way | 64 byte | 800 MHz/1 GHz
Heterogeneous-3 | 8/32 Kbyte | 4 way | 64 byte | 800 MHz/2 GHz

## Slide 18: Results – Heterogeneous Core Specialization
Chart: EDP normalized to the homogeneous core system
| iirflt01-basefp01 | tblook01-puwmod01 | puwmod01-mpeg2encode | g721decode-iirflt01 | g721decode-pntrch01 | iirflt01-ttsprk01 | rspeed01-mpeg2decode | aifftr01-mpeg2decode | g721encode-bitmnp01 | a2time01-cacheb01 | pntrch01-basefp01 | mpeg2encode-iirflt01 | tblook01-g721decode | puwmod01-djpeg | bitmnp01-g721decode | canrdr01-aifftr01 | average | standard deviation
Heterogeneous-1 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.86376 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.86421 | 0.8642 | 0.86422 | 0.863 | 0.86422 | 0.29654 | 0.84054 | 0.14189
Heterogeneous-2 | 1.0971 | 1.0967 | 1.0972 | 1.0958 | 1.0952 | 1.1014 | 1.1189 | 1.1274 | 1.0958 | 1.0961 | 1.0962 | 1.0971 | 1.0958 | 1.1506 | 1.0958 | 0.38686 | 1.0749 | 0.17991
Heterogeneous-3 | 0.83706 | 0.83707 | 0.83707 | 0.83706 | 0.83661 | 0.83706 | 0.83699 | 0.83707 | 0.83707 | 0.83707 | 0.83705 | 0.83705 | 0.83706 | 0.83363 | 0.83706 | 0.28722 | 0.815 | 0.1374
Heterogeneous-1:
16% EDP savings
Heterogeneous-2:
7% EDP increase
Heterogeneous-3:
19% EDP savings
Heterogeneous-1 | 16/32 Kbyte | 4 way | 64 byte | 1/2 GHz
Heterogeneous-2 | 8/16 Kbyte | 4 way | 64 byte | 800 MHz/1 GHz
Heterogeneous-3 | 8/32 Kbyte | 4 way | 64 byte | 800 MHz/2 GHz
Increased core diversity with effective scheduling enhances benefits of heterogeneity!

## Slide 19: Results – Configurable Core Specialization
Chart: EDP normalized to the homogeneous core system
| iirflt01-basefp01 | mpeg2encode-rspeed01 | tblook01-puwmod01 | puwmod01-mpeg2encode | canrdr01-tblook01 | g721decode-iirflt01 | g721decode-pntrch01 | tblook01-mpeg2encode | iirflt01-ttsprk01 | rspeed01-mpeg2decode | g721encode-mpeg2encode | aifftr01-mpeg2decode | g721encode-bitmnp01 | a2time01-cacheb01 | mpeg2decode-canrdr01 | pntrch01-basefp01 | mpeg2encode-iirflt01 | puwmod01-canrdr01 | tblook01-g721decode | puwmod01-djpeg | djpeg-bitmnp01 | bitmnp01-g721decode | canrdr01-aifftr01 | iirflt01-bitmnp01 | average | standard deviation
Test scenario 1 | 0.86528 | 0.86577 | 0.86497 | 0.86539 | 0.86495 | 0.86426 | 0.8638 | 0.86495 | 0.86869 | 0.88247 | 0.86426 | 0.88919 | 0.86426 | 0.86448 | 0.88245 | 0.86459 | 0.86526 | 0.86481 | 0.86426 | 0.90749 | 0.90997 | 0.86426 | 0.30511 | 0.86526 | 0.84776 | 0.11635
Test scenario 2 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.8642 | 0.86422 | 0.86376 | 0.8642 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.86422 | 0.86421 | 0.8642 | 0.86422 | 0.86422 | 0.863 | 0.86537 | 0.86422 | 0.29654 | 0.8642 | 0.84054 | 0.11587
Test scenario 3 | 0.98324 | 0.72844 | 0.72844 | 0.72844 | 1 | 1 | 0.99947 | 1 | 0.72844 | 0.34311 | 1 | 0.72662 | 0.72844 | 0.72844 | 0.72844 | 1 | 0.99996 | 0.72844 | 0.99996 | 0.99907 | 0.99957 | 0.99999 | 0.34229 | 0.99988 | 0.84253 | 0.20151
Test scenario 4 | 0.72844 | 0.72844 | 0.72844 | 0.72844 | 0.72843 | 0.72844 | 0.72805 | 0.72843 | 0.72844 | 0.72844 | 0.72844 | 0.72662 | 0.72844 | 0.72844 | 0.72844 | 0.72843 | 0.72843 | 0.72844 | 0.72844 | 0.72741 | 0.72941 | 0.72844 | 0.24928 | 0.72843 | 0.70838 | 0.097788
Naively-scheduled Heterogeneous-1:
15% EDP savings
Optimally-scheduled Heterogeneous-1:
16% EDP savings
Configurable homogeneous:
16% EDP savings
Configurable heterogeneous:
29% EDP savings
Configurable | 16 – 32 Kbyte | 1 – 4 way | 16 – 64 byte | 1 – 2 GHz
Heterogeneous-1 | 16/32 Kbyte | 4 way | 64 byte | 1/2 GHz
Independently tuned configurable heterogeneous cores achieves maximum EDP savings!

## Slide 20: Conclusions
Evaluated tradeoffs of heterogeneity and configurability in system specialization
  Quantified EDP savings for heterogeneity, configurability, and configurable heterogeneity compared to homogeneous cores
  Provided insights and guidelines for designers
    Best EDP savings achieved with configurable heterogeneous cores
      Configurable heterogeneous cores leverage benefits of heterogeneity and configurability
Future work
  Explore and evaluate the impact of reducing configurable heterogeneous cores’ design space by configuration subsetting

## Slide 21: Future Work
Configuration design space subsetting
  Viana ’06
Application domains
Automotive control
Network protocol
Image Filtering
Configuration subset
Configuration space
Tuning searches a significantly
reduced design space!

## Slide 22: Questions?